## Slide 1: Information-Centric Networks
Section # 4.1: Routing Issues
Instructor: George Xylomenos
Department: Informatics

## Slide 2: Funding
These educational materials have been developed as part of the instructors educational tasks.
The “Athens University of Economics and Business Open Courses” project only funded the reformatting of these educational materials.
The project is being implemented as part of the Operational Program “Instruction and Lifelong Learning” and is co-financed by the European Union (European Social Fund) and national funds.

## Slide 3: Licencing
These educational materials are subject to a Creative Commons License.

## Slide 4: Week 4 / Paper 1
Open issues in Interdomain Routing: a survey
  Marcelo Yannuzzi, Xavier Masip-Bruin, Olivier Bonaventure
  IEEE Network, Nov.-Dec. 2005, vol. 19, no. 6, pp. 49 – 56
Main point
  There are many challenges in interdomain routing
  Relationships between challenges
  Review of problems and proposed solutions
  Reasons for non-adoption of solutions

## Slide 5: Introduction
Limitations of BGP
  Hard to replace due to widespread deployment
  Growth of Internet strains the protocol
Routing among distinct domains
  Independent management of domains
  Active competition between providers
Basics of interdomain routing
  Autonomous System (AS): a distinct network on the Internet
    Managed by a single authority
    Common internal routing policy
    Intradomain routing via IS-IS or OSPF
  More than 20000 ASes in the Internet

## Slide 6: Basics of interdomain routing
Types of ASes
  Single homed stub ASes
    The “leaves” of the network
  Multi homed stub ASes
    Load balancing or failure resiliency
  Transit ASes
Types of AS relationships
  Costumer-provider
  Peer-peer
The AS hierarchy
  Tier-1 (no upstream provider) composing the internet core
  Tier-2 are customers of Tier-1 and providers of Tier-2
  ASes also use peering links to directly exchange traffic

## Slide 7: Basics of interdomain routing
Interior and exterior BGP
  BGP routers exchange reachability information via eBGP
  This information is distributed internally via iBGP
Route discovery and selection
  BGP routers advertise AS level paths to IP prefixes
    There is no global topology view
    The path is abstracted into AS numbers
  Route selection is heavily policy influenced
    Choose the route with the highest local preference
    Choose the route with the shortest AS path
    Choose the route with the lowest Multi Exit Discriminator
    Prefer the route with the lowest IGP metric
    Run tie-breaking rules

## Slide 8: Research challenges
Limited traffic engineering capabilities
  Only reachability is advertised
    No way to propagate multiple routes
  Inbound traffic is hard to control with BGP
    It is the sender and not the receiver that chooses paths
    This is due to the uncoordinated routing on the Internet
Lack of QoS support
  Many ASes have deployed differentiated services
  These allow coarse grained intradomain QoS
  But BGP does not allow interdomain QoS
  Most ASes prefer over-provisioning instead of QoS

## Slide 9: Research challenges
How has the Internet changed?
  AS numbers have swelled
  Connections per AS have increased
  Additional applications
    Application requirements are not reflected into BGP
Slow convergence and chattiness
  BGP messages: Open, Update, Notification, Keepalive
  A failure causes large amounts of BGP updates
    Path exploration takes place until convergence
  BGP routers wait for MRAI before updating a route
  BGP routers often employ route flap damping
    Ignore routes that change too often
  Improve stability at the expense of convergence

## Slide 10: Research challenges
Slow convergence and chattiness
  Proposal: faster propagation of updates due to failures
    Two methods, ghost flushing and reporting the root cause
    Limits path exploration
    Requires BGP modification to indicate a failure cause
    Very hard to pinpoint a failure due to route aggregation
    Route disaggregation impacts scalability, so there is a tradeoff
  Proposal: infer source of failures by correlating data
    Requires multiple vantage points and offline processing
  Each solution adversely affects some objectives
    Solutions: root-cause, MRAI timer, flap damping, aggregation
    Objectives: scalability, convergence, message load

## Slide 11: Research challenges
Scalability problems due to multihoming
  Many stub ASes are multihomed
    Resilience and load balancing
  Each such AS has multiple IP prefixes (one per provider)
    Each prefix is advertised to all providers
    Different paths are advertised to indicate route preference
    Depending on provider aggregation rules, there may be problems
    Eventually, disaggregation may be required to achieve policy goals
    Also, each provider can only aggregate its own prefixes
    All these lead to even more routes being advertised
  Proposal: route filtering
    Avoid propagating very long prefixes (very specific routes)
    This inhibits load balancing (it hides some routes)
  What we really need is better support for multihoming

## Slide 12: Research challenges
Expresiveness and safety of policies
  Each domain independently chooses its policies
  The result is suboptimal due to lack of coordination
    Global routing anomalies arise
    Global divergence of routing policies
  BGP policies are not that expressive
    Rich enough to express intricate routing policies
    Not rich enough to allow discovery of problems
  Each AS does not want to disclose its internal details
    Many problems are hidden inside the AS’s network

## Slide 13: Research challenges
Robustness of BGP sessions
  BGP routers communicate via TCP
  Network congestion can lead to failures
    Hard to resolve congestion due to routing problems
  Need to distinguish routing messages from ordinary traffic
Security issues
  Spoofed TCP RSTs can bring down BGP sessions
    Also spoofed TCP messages can be inserted
    Filter spoofed packets
    Use authentication between BGP routers
  BGP advertisements are not authenticated
    S-BGP certifies the validity of routes by signatures
    Processing cost and need for a PKI

## Slide 14: Research challenges
Lack of multipath routing
  BGP routers only advertise a single path per prefix
    Even if they have received many alternatives
  BGP routers may only use a single path per prefix
    Some implementations use many for load balancing
  Proposed extensions raise scalability concerns
Transit through an AS: iBGP issues
  A large AS has trouble propagating routes inside it
    Ideally all internal routers should communicate with each other
    This not scalable for large ASes
    Different routers may treat traffic differently
  Encapsulation: guarantees that packets will use preferred routes
    Operates between ingress and egress BGP routers

## Slide 15: End of Section # 4.1
Course: Information-Centric Networks, Section # 4.1: Routing Issues
Instructor: George Xylomenos, Department: Informatics