## Slide 1: Information-Centric Networks
Section # 7.3: Evolved Addressing & Forwarding
Instructor: George Xylomenos
Department: Informatics

## Slide 2: Funding
These educational materials have been developed as part of the instructors educational tasks.
The “Athens University of Economics and Business Open Courses” project only funded the reformatting of these educational materials.
The project is being implemented as part of the Operational Program “Instruction and Lifelong Learning” and is co-financed by the European Union (European Social Fund) and national funds.

## Slide 3: Licencing
These educational materials are subject to a Creative Commons License.

## Slide 4: Week 7 / Paper 3
Accountable Internet Protocol (AIP)
  Michael Walfish, Hari Balakrishnan and Scott Shenker David G. Andersen, Hari Balakrishnan, Nick Feamster, Teemu Koponen, Daekyeong Moon, Scott Shenker
  ACM SIGCOMM 2008
Main point
  Accountability at the forefront of the Internet
    Prevention of source spoofing, DoS, route hijacking, route forgery
  AIP uses a hierarchy of self-certifying addresses
  Each component is derived from a public key

## Slide 5: Introduction
The Internet is rife with IP level vulnerabilities
  Misconfigured routers wreak havoc on packet delivery
  Hijacked routes used to send untraceable spam
  Hijacked hosts spoof source addresses
  DoS attacks occur on a daily basis
Many solutions proposed, but all have shortcomings
  Complicated mechanisms that change the Internet model
  External sources of trust to certify BGP updates
  Operator vigilance to keep updating filters
Maybe the fundamental architecture is at fault
  AIP uses self-certifying flat addresses
    Hosts can prove they own an address without a PKI
    But, flat addressing is a scalability challenge

## Slide 6: AIP design
Basic structure and function
  Hierarchical addresses with two or more components
  Each network is divided into Accountability Domains (ADs)
  Each host is an Endpoint IDentifier (EID)
    Both AD and EID are globally unique
    Addresses have the form AD:EID
  ADs may be subdivided into units
    In general addresses are AD1:AD2:…:ADk:EID
  The AD and EID is the hash of the public key of an entity
    Each component is 160 bits long (8+144+8)
    Direct link between identity (public key) and name (AD/EID)
  Each AD/EID has the form Version:Key Hash:Interface
    Version indicates the scheme used to generate the AD/EID
    Interface indicates one of the interfaces of a host

## Slide 7: AIP design
Forwarding and routing
  Each packet contains source and destination AD:EID
  Multiple AD levels are treated as a stack
    Forwarding proceeds towards the current AD
    Border routers switch to the next AD in the stack
  Interdomain routing can use BGP or any other protocol
    Routers advertise reachability to ADs, not prefixes
    ADs can be grouped into ASes if needed
DNS and mobility
  A multihomed host will have different ADs but the same EID
  Transport protocols bind to the EID, not the AD
  Mobile hosts need to change their AD only
  Changes can be authenticated since EIDs are bound to keys

## Slide 8: Uses of accountability
Source accountability (no source spoofing)
  Common source spoofing variants
    Pretending to be a host at another network
    Pretending to be another host at your network
    Creating large numbers of unused addresses
  EID verification: at first hop router
    On reception of data from unverified host
      Drop packet and return verification packet V
      V contains source/destination addresses, packet hash and interface
      V is signed using a secret that changes regularly
      The sender returns V signed with its private key
      The router verifies the signature and if correct passes next packets
      Replay attacks at the router prevented by the secret
      Replay attacks at the sender prevented by inserting random packet ID
      Only the sender needs to cache hashes of recent packets

## Slide 9: Uses of accountability
Source accountability (no source spoofing)
  AD verification (at AD boundaries)
    On reception of packet from AD B, AD A checks that:
      If B is trusted to check packets, forward it
      Otherwise check if the packet is on the route to the source
      Otherwise drop packet and verify the source as with the EID
      The last step allows multihoming and asymmetric paths
  Ensuring scalability at border routers
    Only packets that arrive from an unexpected route are remembered
    If the AD:EID pairs for the same AD are many, use a wildcard AD:*
    This is dangerous if an attacker controls some hosts in the AD
      It can force the border router to insert a wildcard
  Limiting address minting
    Routers can limit the number of new EIDs they accept per minute
    Similarly for ADs in border routers

## Slide 10: Uses of accountability
Shut-off protocol
  Requires a smart-NIC that rate-limits transmission if needed
    The NIC records hashes of recently sent packets
    It also accepts Shut-Off Packets (SOPs) independently
    A SOP contains a packet hash and a TTL, signed by the destination
    The NIC accepts the packet if it contains a valid hash and signature
    Then it shuts-off traffic for the TTL
    The random packet ID prevents replay attacks
    Hashes of thousands of packet can be kept in a Bloom filter
Securing BGP
  BGP peering sessions are encrypted with AD public keys
  BGP routers sign their routing announcements
  Routers only need to know the public keys of other ADs

## Slide 11: Routing scalability
Routing growth estimates
  The AS diameter increases slowly (less than 5 hops)
  Routing tables grow 17% per year (about 1.6 million in 2020)
  Routing traffic grows linearly with table size
    Estimate 1.5 updates per day per prefix
Effects of moving to AIP
  RIB/FIB size increase due to 160 bit AD and 2048 bit public key
    Doubles for two level ADs
  BUT: lookups are flat, not longest prefix
    Estimated 80% reduction in memory accesses
  The AS diameter may grow by 2-3 hops due to two level ADs
  CPU costs that same as those needed for S-BGP

## Slide 12: Routing scalability
Semiconductor growth trends
  Assume the ITRS roadmap of density doubling every 3 years
Resource requirements
  RIB (DRAM): Roughly triple the amount of RAM needed by IP
    No problem with current growth trends
  FIB (DR/SR/CAM): SRAM will grow much faster than FIBs
  CPU: Loading time of tables to memory
    Estimated to be less than 30 seconds
  Cryptography: 66 seconds for all tables
    May need acceleration as it is slower than the loading time

## Slide 13: Key management
Key compromise: what if a private key is exposed?
  Key revocation is tricky but feasible
  The biggest problem is the false confidence in lost keys
    Therefore mechanisms for rapid loss detection are needed
  Public registries for ADs are needed
    They only store self certifying data (no PKI needed)
    Can be automatically populated (no human intervention)
    Local (per domain) and global registries possible
  Types of information stored in registries
    Identity/public key pairs
    Revoked public keys, signed by private keys (write once!)
    Peering relationships, signed by both peers
    Certificates binding EIDs to ADs (may be multiple)
    Certificates binding EIDs to first hop routers (can be multiple)

## Slide 14: Key management
Maintaining domain registries
  Domains should be forced to sign AD:EID to get it into DNS
  Hosts check the registries of the domains hosting them
  Domains check the registries of their peers
Key discovery: what is the destination address?
  Use DNS and verify keys against AD identifiers
  Establish out-of-band trust between peering domains
Cryptographic algorithm compromise
  This is why version numbers are added to identities
  New algorithms can co-exist with older ones
  A version number indicates a hash/sign combination pair

## Slide 15: Traffic engineering and AD size
Traffic engineering maps offered load to a set of paths
  Performed by DNS and selective prefix advertising
  ADs cannot be split to smaller prefixes for control
    But they can be split hierarchically
  AD granularity: a set of hosts under common administration
  Splitting ADs for traffic engineering can be done
    It is aggregating these prefixes that is impossible!
  Experiments show that such aggregation is quite rare
  Another possibility is to use the interface bits
    Each interface could be advertised separately
    Allows aggregation by zeroing out the interface bits
  DNS load balancing does not change
    The interface bits can make it easier

## Slide 16: End of Section # 7.3
Course: Information-Centric Networks, Section # 7.3: Evolved Addressing & Forwarding
Instructor: George Xylomenos, Department: Informatics