## Slide 1: Information-Centric Networks
Section # 7.2: Evolved Addressing & Forwarding
Instructor: George Xylomenos
Department: Informatics

## Slide 2: Funding
These educational materials have been developed as part of the instructors educational tasks.
The “Athens University of Economics and Business Open Courses” project only funded the reformatting of these educational materials.
The project is being implemented as part of the Operational Program “Instruction and Lifelong Learning” and is co-financed by the European Union (European Social Fund) and national funds.

## Slide 3: Licencing
These educational materials are subject to a Creative Commons License.

## Slide 4: Week 7 / Paper 2
NIRA: A New Inter-Domain Routing Architecture
  Xiaowei Yang, David Clark, Arthur W. Berger
  IEEE/ACM TRANSACTIONS ON NETWORKING, VOL. 15, NO. 4, AUGUST 2007
Main point
  Users choose ISPs but ISPs choose routes
  What if users could choose provider level routes?
    How do you discover routes?
    How do you represent routes?
    How do you switch routes quickly?
    How are providers compensated?
  NIRA represents routes as a sender and receiver part
    Each part is represented as a single address

## Slide 5: Introduction
Consider routes at the AS level
  Users select ISPs only
  ISPs interconnect independently
Why have users control routes?
  With cable against DSL local competition is very slim
  Route selection introduces competition at the top level
    Gives backbone ISPs an incentives to invest
BGP selected routes are not always the best
  For almost 80% of paths, better ones can be found
  Even more opportunities for multihomed hosts
  Users know whether they prefer (say) latency or bandwidth
NIRA provides route selection at the domain level
  More manageable than the router level

## Slide 6: Design overview
Basic concepts
  A user can only select routes for which he pays for
  Route consists of sender, core and receiver part
    Source and destination part represented as a single address
Design rationale
  Users need to discover failure free routes
  Routes must be encoded into packets
  Providers must be compensated
    Assume bilateral contracts between providers
    Contracts are typically customer-provider or peer-to-peer
    Tier-1 providers do not purchase transit from others
    The Internet core consists of the Tier-1 providers

## Slide 7: Design overview
Route discovery
  Users can only see their providers, recursively up to the core
    Including the peering connections outside the core
  This is the up-graph of the user
    Represented as one route per domain and one link between domains
  Topology information propagation protocol (TIPP)
  TIPP path-vector component
    Advertises reachability towards the core
    Tier-1 providers advertise themselves, customers attach themselves
  TIPP link-state component
    Advertises network dynamics within provider hierarchy
  A sender combines an up-graph and a reverse up-graph
    Valley-free routes: upward, horizontal, downward

## Slide 8: Design overview
Efficient route representation
  NIRA encodes a path through an up-graph into a single address
    Both sender and receiver fit into single addresses
  Each Tier-1 provider obtains a globally unique address prefix
    This is subdivided to its customers, recursively
    The final address encodes all the providers it is using
  NIRA uses 128 bit IPv6 addresses
    96 bits encode the up-graph and 32 bits a host in the ISP
    Could instead use a sequence of IPv4 addresses
  Peering links use a private address space
    They are also recursively allocated to customers
  Each host eventually obtains a set of addresses
    Each address encodes a path to the core or to a peering domain

## Slide 9: Design overview
Bootstrap communication
  How do you find out the receiver’s addresses?
    Need to select a path for the receiver too!
  NRLS: maps names to route segments
    Similar to DNS but returns multiple up-graphs
  Hosts are notified by TIPP about network changes
    They may then need to notify NLRS about their routes
Handling route failures
  TIPP notifies the sender but not the receiver
  If a route is unavailable, the routers return ICMP errors
    Local errors are masked in domain level paths
    Inter-domain errors are passed to the sender for a decision
    The sender consults the NLRS again to choose a new route

## Slide 10: Design overview
Choosing routes
  A user agent runs on each user’s computer
  The agent combines sender and receiver parts
  Depending on preferences it chooses a combination
    Subsequent packets can be used to switch to another route
Forwarding
  The up-graphs and reverse up-graphs are specified
  The route through the core is not specified
    Tier-1 providers retain control of these routes
    Users are not exposed to the dense backbone connectivity
    Each Tier-1 provider needs to advertise a single prefix
  Any ISP (not only Tier-1’s) can decide to join the core
    It simply needs to obtain a global prefix

## Slide 11: TIPP
TIPP runs between domains but not in the core
  Separate address and topology propagation
  Propagating address information
    A provider announces address prefixes to customers
    Customers recursively propagate these announcements
  Propagating topology information
    Link-state protocol with policy controls
  Scope enforcement: limit what neighbors know about customers
  Information hiding: limit what neighbors know about neighbors
  Uses the Shortest Path Topology Algorithm (SPTA)
    Computationally more expensive than OSPF or IS-IS
    But easier to resolve inconsistencies between different messages
    Should be sufficient for the small scale of the upgraphs

## Slide 12: Forwarding
What is the next hop towards a destination address?
  Three tables are maintained at each router
    Uphill: points to the provider that allocated each prefix
    Downhill: points to the customer that received each prefix
    Bridge: points to the neighbor allocated with each private prefix
  Separate from other routing tables (for core routers)
  Lookup destination in downhill table
  Lookup source in uphill table
  Special entries in uphill table
    Routing: forward through the core
    Bridge: forward via bridge table (to peer)
  Special entries in downhill table
    Blackhole: drop packet (customer is disconnected)
    Self: forward packet inside the domain

## Slide 13: Evaluation
Amount of state obtained from TIPP
  The up-graph can grow exponentially
    Provider hierarchy is not fully known, but inferred
  Statistics for 90% of domains
    Less than 20 addresses prefixes
    Less than 30 link records
    Less than 100 forwarding entries
Message overhead and convergence speed of TIPP
  Less than 1 sec to converge after link failure/recovery
  Less than 2 messages per link failure/recovery
Setup latency due to reactive failure detection (ICMP)
  80% of connections need a round trip
  99% need three round trips

## Slide 14: End of Section # 7.2
Course: Information-Centric Networks, Section # 7.2: Evolved Addressing & Forwarding
Instructor: George Xylomenos, Department: Informatics