## Slide 1: Information-Centric Networks
Section # 10.3: Publish/Subscribe
Instructor: George Xylomenos
Department: Informatics

## Slide 2: Funding
These educational materials have been developed as part of the instructors educational tasks.
The “Athens University of Economics and Business Open Courses” project only funded the reformatting of these educational materials.
The project is being implemented as part of the Operational Program “Instruction and Lifelong Learning” and is co-financed by the European Union (European Social Fund) and national funds.

## Slide 3: Licencing
These educational materials are subject to a Creative Commons License.

## Slide 4: Week 10 / Paper 3
Illustrating a publish-subscribe Internet architecture
  Nikos Fotiou, Dirk Trossen, George C. Polyzos:
  Telecommunication Systems (to appear)
Main point
  PSIRP = Publish-Subscribe Internet Routing Paradigm
  Totally clean slate architecture
    Supports availability, security and mobility
    Opportunities for innovative applications

## Slide 5: Introduction
The Internet has not changed a lot since its inception
  Still reminiscent of the telephone network
    Connect two endpoints via the network infrastructure
User needs have changed a lot in the meantime
  Endpoints do not trust each other
  Receivers cannot avoid sender traffic
  Content is delivered via CDNs and P2P applications
  Applications do not care which endpoint provides the content
  Middleboxes try to fix each problem separately
The publish-subscribe paradigm
  Centered on information, not endpoints
  Receivers only get what they asked for (via subscriptions)

## Slide 6: Introduction
Components of a publish-subscribe system
  Publishers: feed information to the system
  Subscribers: consume published information
  Brokers: forward data from publishers to subscribers
  Rendezvous Nodes: match publications with subscriptions
    Initiation of delivery from publishers to subscribers
Advantages of publish-subscribe
  Publishers and subscribers are decoupled in time and space
    Publishers are not aware of subscribers and vice versa
    Publications and subscriptions are not synchronized
  Multicast can be taken advantage of
PSIRP: EU funded project that builds a pub-sub system
  Continued by PURSUIT

## Slide 7: The PSIRP architecture
Publications
  Information becomes available via publications
    Any size, from data chunks to entire movies
  Identified by a Rendezvous Identifier (RId)
    Flat and unique within a scope
Scopes
  Containers for publications
    Any type of grouping, from social networks to network areas
  Identified by a Scope Identifier (SId)
    Flat and unique within a scope
  Hierarchical organization of scopes
  Access control is based on scopes
    Who can issue or access publications within a scope?

## Slide 8: The PSIRP architecture
Publishing data
  A RId is derived by an application specific function
  The proper SId is selected to organize and control information
  The responsible Rendezvous Node for the scope is contacted
    This node is called the Rendezvous Point (RP) for the scope
  The publication metadata is sent to the RP
    Metadata can indicate that a publication is divided into pieces
    The RId’s for the pieces may be algorithmically related
Subscribing to data
  Need to know the SId/RId of the publication
  The RP for the scope is contacted
  The RP initializes forwarding from publisher to subscriber

## Slide 9: The PSIRP architecture
Forwarding in PSIRP
  A topology formation function creates delivery paths
  A path is denoted by a Forwarding Identifier (FId)
  The RP makes sure the FId is sent to the subscriber
  The Publisher sends the publication with the FId
  Brokers forward the publication using the FId
Caching in PSIRP
  Any node can cache publications it is forwarding
  It then becomes a source for these publications
Multicasting
  When multiple subscribers exist, publications are multicast

## Slide 10: Current solutions
Note: this reflects the current PURSUIT status
Rendezvous
  Use of a hierarchical DHT to assign scopes to RPs
    Ideally the RP should be close to the publisher
  DHTs have a tendency to violate routing policies though!
Forwarding
  Use of the LIPSIN source routing mechanism
    Unicast is a special case of multicast
  How are interdomain paths handled?
Topology management
  Link-state protocol (like OSPF) for topology discovery
  Dijkstra’s algorithm for intra-domain shortest paths
  How do multiple domains co-ordinate routing?

## Slide 11: Application development issues
Many open issues at the fundamental level
Publication identifiers
  Not obvious how the RId can be determined
    It has to be unique within a scope (or more!)
  How will algorithmic identifiers work?
    Does the network know how they are generated?
Publication scoping
  How visible are scopes to applications?
    They may be used only at a low level
Trust in transactions
  Which nodes can be trusted to provide services?
    Which RP is the correct one?

## Slide 12: Development status
Two prototypes available
  Blackhawk: node prototype for FreeBSD
  Blackadder: network code prototype for Linux
  Both migrating to use the Click modular router framework
    Click is portable and can run in user or kernel space
  Both available on an open source basis
Many things are being tested
  Rendezvous: different DHTs for inter-domain rendezvous
  Forwarding: inter-domain and large group solutions
  Topology: inter-domain topology formation
  Transport: pull-based protocols with multiple sources
  Caching: on-path and off-path solutions
  Mobility: exploit caching to hide disconnections

## Slide 13: End of Section # 10.3
Course: Information-Centric Networks, Section # 10.3: Publish/Subscribe
Instructor: George Xylomenos, Department: Informatics