## Slide 1: Information-Centric Networks
Section # 9.3: Clean Slate
Instructor: George Xylomenos
Department: Informatics

## Slide 2: Funding
These educational materials have been developed as part of the instructors educational tasks.
The “Athens University of Economics and Business Open Courses” project only funded the reformatting of these educational materials.
The project is being implemented as part of the Operational Program “Instruction and Lifelong Learning” and is co-financed by the European Union (European Social Fund) and national funds.

## Slide 3: Licencing
These educational materials are subject to a Creative Commons License.

## Slide 4: Week 9 / Paper 3
VoCCN: Voice Over Content-Centric Networks
  V. Jacobson, D. K. Smetters, N. H. Briggs, M. F. Plass, P. Stewart, J. D. Thornton, R. L. Braynard
  ACM ReArch 2009
Main point
  Content-centric targets fetching/downloading applications
  Can it work for other applications, too?
    E-mail, streaming and (especially) VoIP?
  VoCCN: Voice over CCN (instead of IP)
  Based on certain key properties of CCN

## Slide 5: Introduction
Most new architectures place content at the center
  Good fit for content exchange applications (WWW, P2P)
  What about conversational applications (VoIP, e-commerce)?
VoCCN addresses the issue of CCN suitability
  Real-time, conversational, telephony over CCN
  Simpler, more secure and more scalable than VoIP
  Uses SIP and RTP to securely interoperate with VoIP
  Employs a stateless IP to CCN gateway
  Model for mapping conversational applications to CCN

## Slide 6: VoIP background
VoIP components
  Endpoints are represented by fixed proxies
    The endpoints can be mobile or have dynamic IP addresses
  Signaling established via SIP (Session Initiation Protocol)
    Caller to caller’s proxy, to callee’s proxy, to callee
    The proxies must know where the endpoints reside
  Data exchange directly between endpoints
    The caller’s invite indicates its address for RTP data
    The callee’s accept indicates address for RTP data
  Media can be secured via SRTP or tunneling inside DTLS
  Signaling can be secured via DTLS/PKI or MIKEY
    Authentication and encryption are tricky to setup
    Usually everything ends up unencrypted and unathenticated!

## Slide 7: Architecture
VoIP is harder than it needs to be
  The caller simply wants to talk to the callee
  The network requires finding the callee’s phone IP address
    This is where the SIP proxies come into play
  In content-oriented networking this should be redundant
VoCCN has to solve a different set of problems
  Service rendezvous: the callee must offer a contact point
    In IP this is the TCP/UDP port to which the application listens
  In CCN we must request content that has not been published
    The network must route the request to potential publishers
    The publishers should then create and publish the content

## Slide 8: Architecture
VoCCN has to solve a different set of problems
  The service rendezvous must transition to a conversation
    In IP the SIP packets contain information in an SDP payload
  In CCN we need dynamically constructible names
    Construct the name of a piece of content without being told
Two requirements for content name construction
  Deterministic algorithm to produce names
    Names rely on information available to both endpoints
    Cannot use (say) content hashes as names
  Support for partial specification of names
    Constructing unique names requires prearrangement
    Partial names allow unique names to be used eventually
  Structured names can satisfy both requirements

## Slide 9: Architecture
In CCN content uses hierarchical naming
  Interest packets specify a name prefix and some rules
    The rules specify what matching content to return
  CCN routers use prefix matching to direct Interests
    Sent towards content sources that have registered availability
  Sources do not need to register the exact content, only prefixes
    Content can be generated on the fly
  Data packets reverse the path taken by interests
VoCCN signaling
  Each VoCCN endpoint has an identity (e.g. alice@ccnx.org)
  The endpoint registers to offer data in a specific namespace
    Based on service and identity (e.g. /ccnx.org/sip/alice/invite)

## Slide 10: Architecture
VoCCN signaling
  A caller sends an Interest asking for content from the callee
    The well-known prefix is extended with unique data
    A session key encrypted with the callee’s public key
    The SIP invite data encrypted with the session key
  The callee responds with a data packet generated on the fly
    Uses the name indicated by the caller
    Includes the SIP accept data encrypted with the session key
VoCCN data exchange
  Uses a sequence of names based on rendezvous information
    Call-id+endpoint+sequence (e.g. /ccnx.org/alice/call-id/rtp/seqno)
    Each Interest is matched by a unique data packet
  Can issue many interests to pipeline data flow
    As data packets arrive, more interests are generated

## Slide 11: Advantages
Easy location of endpoints
  In IP the endpoint needs to register its IP address with a proxy
  With CCN a prefix can be registered at many areas
    The Interest will be routed to all of them
    The endpoint will respond from its current location
Endpoints can prove their identity
  All the credentials needed are at the endpoint
    The private key needed to decrypt the session key
  No need to change identity to IP address mappings
Advanced services are easy to build
  Exploits the built-in multipoint routing of CCN
    Follow call requests or copy and process call contents

## Slide 12: VoCCN/VoIP interoperability
Based on a stateless VoCCN/VoIP gateway
  SIP and SRTP are used to simplify the exchange
  The gateway acts as a SIP proxy that translates packets
  A SIP/SRTP packet is translated to a CCN data packet
    They match CCN interest packets from VoCCN endpoints
    The gateway also generates an Interest for the next packet
    This matches the next data packet from the VoCCN endpoint
    The VoCCN packet is translated to an IP packet
  The proxy does not maintain state on conversations
    Every action is based on received packets
  Signaling security is provided for the CCN part only
    The IP part may have its own SIP signaling security mechanism
    End-to-end data security does not involve the gateway

## Slide 13: Implementation
Implementation data
  VoCCN client based on Linphone
    Uses extensible SIP and RTP libraries
    Simple plugins for the CCN part
  CCN routers on all routers and endpoints
    CCN routers communicate over a UDP overlay
Security
  Many ways to get public keys in CCN
    Ask for /ccnx.org/users/alice/KEY and accept on faith
    Publish key as CCN content signed by a trusted third party
  VoCCN used MIKEY to secure the data exchange
    MIKEY is initiated during the SIP signaling exchange
  The signaling exchange is protected with public keys

## Slide 14: Implementation
Performance
  Direct exchange between two machines in the same LAN
  Compared stock Linphone with VoCCN version
  No perceptible impact from packet signing with 1024 bit RSA keys
  No packet loss, but some delayed packets in the latter case
  Similar jitter for both versions

## Slide 15: End of Section # 9.3
Course: Information-Centric Networks, Section # 9.3: Clean Slate
Instructor: George Xylomenos, Department: Informatics