## Slide 1: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 13: Δρομολόγηση σε Κινητά Αδόμητα Δίκτυα (Mobile Ad Hoc Networks)
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2
Slides taken from Nitin H. Vaidya’s Mobicom 2000 tutorial on Mobile Ad Hoc Networks

## Slide 3: Why is Routing in MANET different ?
Host mobility
  link failure/repair due to mobility may have different characteristics than those due to other causes
Rate of link failure/repair may be high when nodes move fast
New performance criteria may be used
  route stability despite mobility
  energy consumption

## Slide 4: Unicast Routing Protocols
Many protocols have been proposed
Some have been invented specifically for MANET
Others are adapted from previously proposed protocols for wired networks
No single protocol works well in all environments
  some attempts made to develop adaptive protocols

## Slide 5: Routing Protocols
Proactive protocols
  Determine routes independent of traffic pattern
  Traditional link-state and distance-vector routing protocols are proactive
Reactive protocols
  Maintain routes only if needed
Hybrid protocols

## Slide 6: Trade-Off
Latency of route discovery
  Proactive protocols may have lower latency since routes are maintained at all times
  Reactive protocols may have higher latency because a route from X to Y will be found only when X attempts to send to Y
Overhead of route discovery/maintenance
  Reactive protocols may have lower overhead since routes are determined only if needed
  Proactive protocols can (but not necessarily) result in higher overhead due to continuous route updating
Which approach achieves a better trade-off depends on the traffic and mobility patterns

## Slide 7: Overview of Unicast Routing Protocols

## Slide 8: Flooding for Data Delivery
Sender S broadcasts data packet P to all its neighbors
Each node receiving P forwards P to its neighbors
Sequence numbers used to avoid the possibility of forwarding the same packet more than once
Packet P reaches destination D provided that D is reachable from sender S
Node D does not forward the packet

## Slide 9: Flooding for Data Delivery
A
Represents that connected nodes are within each
other’s transmission range
Y
Represents a node that has received packet P
B
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 10: Flooding for Data Delivery
Represents transmission of packet P
Represents a node that receives packet P for
the first time
Z
Y
Broadcast transmission
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L

## Slide 11: Flooding for Data Delivery
Node H receives packet P from two neighbors:
potential for collision
Y
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 12: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Node C receives packet P from G and H, but does not forward
it again, because node C has already forwarded packet P once
Z
Y
M
N
L

## Slide 13: Flooding for Data Delivery
Y
Nodes J and K both broadcast packet P to node D
Since nodes J and K are hidden from each other, their
transmissions may collide
=> Packet P may not be delivered to node D at all,
despite the use of flooding
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 14: Flooding for Data Delivery
Y
Node D does not forward packet P, because node D
is the intended destination of packet P
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 15: Flooding for Data Delivery
Flooding completed
Nodes unreachable from S do not receive packet P (e.g., node Z)
Nodes for which all paths from S go through the destination D
also do not receive packet P (example: node N)
Y
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 16: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Flooding may deliver packets to too many nodes
(in the worst case, all nodes reachable from sender
may receive the packet)
Z
Y
M
N
L

## Slide 17: Flooding for Data Delivery: Advantages
Simplicity
May be more efficient than other protocols when rate of information transmission is low enough that the overhead of explicit route discovery/maintenance incurred by other protocols is relatively higher
  this scenario may occur, for instance, when nodes transmit small data packets relatively infrequently, and many topology changes occur between consecutive packet transmissions
Potentially higher reliability of data delivery
  Because packets may be delivered to the destination on multiple paths

## Slide 18: Flooding for Data Delivery: Disadvantages
Potentially, very high overhead
  Data packets may be delivered to too many nodes who do not need to receive them
Potentially lower reliability of data delivery
  Flooding uses broadcasting -- hard to implement reliable broadcast delivery without significantly increasing overhead
      Broadcasting in IEEE 802.11 MAC is unreliable
  In our example, nodes J and K may transmit to node D simultaneously, resulting in loss of the packet
      in this case, destination would not receive the packet at all

## Slide 19: Flooding of Control Packets
Many protocols perform (potentially limited) flooding of control packets, instead of data packets
The control packets are used to discover routes
Discovered routes are subsequently used to send data packet(s)
Overhead of control packet flooding is amortized over data packets transmitted between consecutive control packet floods

## Slide 20: Dynamic Source Routing (DSR) [Johnson96]
When node S wants to send a packet to node D, but does not know a route to D, node S initiates a route discovery
Source node S floods Route Request (RREQ)
Each node appends own identifier when forwarding RREQ

## Slide 21: Route Discovery in DSR
Y
Represents a node that has received RREQ for D from S
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 22: Route Discovery in DSR
Represents transmission of RREQ
Z
Y
Broadcast transmission
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S]
[X,Y] Represents list of identifiers appended to RREQ

## Slide 23: Route Discovery in DSR
Node H receives packet RREQ from two neighbors:
potential for collision
Y
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
[S,E]
[S,C]

## Slide 24: Route Discovery in DSR
Node C receives RREQ from G and H, but does not forward
it again, because node C has already forwarded RREQ once
Y
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
[S,C,G]
[S,E,F]

## Slide 25: Route Discovery in DSR
Y
Nodes J and K both broadcast RREQ to node D
Since nodes J and K are hidden from each other, their
transmissions may collide
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
[S,C,G,K]
[S,E,F,J]

## Slide 26: Route Discovery in DSR
Y
Node D does not forward RREQ, because node D
is the intended target of the route discovery
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
[S,E,F,J,M]

## Slide 27: Route Discovery in DSR
Destination D on receiving the first RREQ, sends a Route Reply (RREP)
RREP is sent on a route obtained by reversing the route appended to received RREQ
RREP includes the route from S to D on which RREQ was received by node D

## Slide 28: Route Reply in DSR
A
Y
B
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
RREP [S,E,F,J,D]
Represents RREP control message

## Slide 29: Route Reply in DSR
Route Reply can be sent by reversing the route in Route Request (RREQ) only if links are guaranteed to be bi-directional
  To ensure this, RREQ should be forwarded only if it received on a link that is known to be bi-directional
If unidirectional (asymmetric) links are allowed, then RREP may need a route discovery for S from node D
  Unless node D already knows a route to node S
  If a route discovery is initiated by D for a route to S, then the Route Reply is piggybacked on the Route Request from D.
If IEEE 802.11 MAC is used to send data, then links have to be bi-directional (since Ack is used)

## Slide 30: Dynamic Source Routing (DSR)
Node S on receiving RREP, caches the route included in the RREP
When node S sends a data packet to D, the entire route is included in the packet header
  hence the name source routing
Intermediate nodes use the source route included in a packet to determine to whom a packet should be forwarded

## Slide 31: Data Delivery in DSR
Y
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
DATA [S,E,F,J,D]
Packet header size grows with route length

## Slide 32: When to Perform a Route Discovery
When node S wants to send data to node D, but does not know a valid route node D

## Slide 33: DSR Optimization: Route Caching
Each node caches a new route it learns by any means
When node S finds route [S,E,F,J,D] to node D, node S also learns route [S,E,F] to node F
When node K receives Route Request [S,C,G] destined for node, node K learns route [K,G,C,S] to node S
When node F forwards Route Reply RREP [S,E,F,J,D], node F learns route [F,J,D] to node D
When node E forwards Data [S,E,F,J,D] it learns route [E,F,J,D] to node D
A node may also learn a route when it overhears Data packets

## Slide 34: Use of Route Caching
When node S learns that a route to node D is broken, it uses another route from its local cache, if such a route to D exists in its cache. Otherwise, node S initiates route discovery by sending a route request
Node X on receiving a Route Request for some node D can send a Route Reply if node X knows a route to node D
Use of route cache
  can speed up route discovery
  can reduce propagation of route requests

## Slide 35: Use of Route Caching
[P,Q,R] Represents cached route at a node
(DSR maintains the cached routes in a tree format)
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,E,F,J,D]
[E,F,J,D]
[C,S]
[G,C,S]
[F,J,D],[F,E,S]
[J,F,E,S]
Z

## Slide 36: Use of Route Caching: Can Speed up Route Discovery
Z
When node Z sends a route request
for node C, node K sends back a route
reply [Z,K,G,C] to node Z using a locally
cached route
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,E,F,J,D]
[E,F,J,D]
[C,S]
[G,C,S]
[F,J,D],[F,E,S]
[J,F,E,S]
RREQ
[K,G,C,S]
RREP

## Slide 37: Use of Route Caching: Can Reduce Propagation of Route Requests
A
Z
Assume that there is no link between D and Z.
Route Reply (RREP) from node K limits flooding of RREQ.
In general, the reduction may be less dramatic.
B
S
E
F
H
J
D
C
G
I
K
Y
M
N
L
[S,E,F,J,D]
[E,F,J,D]
[C,S]
[G,C,S]
[F,J,D],[F,E,S]
[J,F,E,S]
RREQ
[K,G,C,S]
RREP

## Slide 38: Route Error (RERR)
Y
J sends a route error to S along route J-F-E-S when its attempt to forward the data packet S (with route SEFJD) on J-D fails
Nodes hearing RERR update their route cache to remove link J-D
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
RERR [J-D]

## Slide 39: Route Caching: Beware!
Stale caches can adversely affect performance
With passage of time and host mobility, cached routes may become invalid
A sender host may try several stale routes (obtained from local cache, or replied from cache by other nodes), before finding a good route
An illustration of the adverse impact on TCP will be discussed later in the tutorial [Holland99]

## Slide 40: Dynamic Source Routing: Advantages
Routes maintained only between nodes who need to communicate
  reduces overhead of route maintenance
Route caching can further reduce route discovery overhead
A single route discovery may yield many routes to the destination, due to intermediate nodes replying from local caches

## Slide 41: Dynamic Source Routing: Disadvantages
Packet header size grows with route length due to source routing
Flood of route requests may potentially reach all nodes in the network
Care must be taken to avoid collisions between route requests propagated by neighboring nodes
  insertion of random delays before forwarding RREQ
Increased contention if too many route replies come back due to nodes replying using their local cache
  Route Reply Storm problem
  Reply storm may be eased by preventing a node from sending RREP if it hears another RREP with a shorter route

## Slide 42: Dynamic Source Routing: Disadvantages
An intermediate node may send Route Reply using a stale cached route, thus polluting other caches
This problem can be eased if some mechanism to purge (potentially) invalid cached routes is incorporated.
For some proposals for cache invalidation, see [Hu00Mobicom]
  Static timeouts
  Adaptive timeouts based on link stability

## Slide 43: Ad Hoc On-Demand Distance Vector Routing (AODV) [Perkins99Wmcsa]
DSR includes source routes in packet headers
Resulting large headers can sometimes degrade performance
  particularly when data contents of a packet are small
AODV attempts to improve on DSR by maintaining routing tables at the nodes, so that data packets do not have to contain routes
AODV retains the desirable feature of DSR that routes are maintained only between nodes which need to communicate

## Slide 44: AODV
Route Requests (RREQ) are forwarded in a manner similar to DSR
When a node re-broadcasts a Route Request, it sets up a reverse path pointing towards the source
  AODV assumes symmetric (bi-directional) links
When the intended destination receives a Route Request, it replies by sending a Route Reply
Route Reply travels along the reverse path set-up when Route Request is forwarded

## Slide 45: Route Requests in AODV
A
Y
Represents a node that has received RREQ for D from S
B
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 46: Route Requests in AODV
Represents transmission of RREQ
Z
Y
Broadcast transmission
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L

## Slide 47: Route Requests in AODV
A
Represents links on Reverse Path
Y
B
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 48: Reverse Path Setup in AODV
Node C receives RREQ from G and H, but does not forward
it again, because node C has already forwarded RREQ once
Y
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 49: Reverse Path Setup in AODV
Y
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 50: Reverse Path Setup in AODV
Y
Node D does not forward RREQ, because node D
is the intended target of the RREQ
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 51: Route Reply in AODV
Y
Represents links on path taken by RREP
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L

## Slide 52: Route Reply in AODV
An intermediate node (not the destination) may also send a Route Reply (RREP) provided that it knows a more recent path than the one previously known to sender S
To determine whether the path known to an intermediate node is more recent, destination sequence numbers are used
The likelihood that an intermediate node will send a Route Reply when using AODV not as high as DSR
  A new Route Request by node S for a destination is assigned a higher destination sequence number. An intermediate node which knows a route, but with a smaller sequence number, cannot send Route Reply

## Slide 53: Forward Path Setup in AODV
A
Y
B
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
Forward links are setup when RREP travels along
the reverse path
Represents a link on the forward path

## Slide 54: Data Delivery in AODV
Y
Routing table entries used to forward data packet.
Route is not included in packet header.
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
DATA

## Slide 55: Timeouts
A routing table entry maintaining a reverse path is purged after a timeout interval
  timeout should be long enough to allow RREP to come back
A routing table entry maintaining a forward path is purged if not used for a active_route_timeout interval
  if no data is being sent using a particular routing table entry, that entry will be deleted from the routing table (even if the route may actually still be valid)

## Slide 56: Link Failure Reporting
A neighbor of node X is considered active for a routing table entry if the neighbor sent a packet within active_route_timeout interval which was forwarded using that entry
When the next hop link in a routing table entry breaks, all active neighbors are informed
Link failures are propagated by means of Route Error messages, which also update destination sequence numbers

## Slide 57: Route Error
When node X is unable to forward packet P (from node S to node D) on link (X,Y), it generates a RERR message
Node X increments the destination sequence number for D cached at node X
The incremented sequence number N is included in the RERR
When node S receives the RERR, it initiates a new route discovery for D using destination sequence number at least as large as N

## Slide 58: Destination Sequence Number
Continuing from the previous slide …
When node D receives the route request with destination sequence number N, node D will set its sequence number to N, unless it is already larger than N

## Slide 59: Link Failure Detection
Hello messages: Neighboring nodes periodically exchange hello message
Absence of hello message is used as an indication of link failure
Alternatively, failure to receive several MAC-level acknowledgement may be used as an indication of link failure

## Slide 60: Why Sequence Numbers in AODV
To avoid using old/broken routes
  To determine which route is newer
To prevent formation of loops
  Assume that A does not know about failure of link C-D because RERR sent by C is lost
  Now C performs a route discovery for D. Node A receives the RREQ (say, via path C-E-A)
  Node A will reply since A knows a route to D via node B
  Results in a loop (for instance, C-E-A-B-C )
A
B
C
D
E

## Slide 61: Why Sequence Numbers in AODV
A
B
C
D
E
  Loop C-E-A-B-C

## Slide 62: Optimization: Expanding Ring Search
Route Requests are initially sent with small Time-to-Live (TTL) field, to limit their propagation
  DSR also includes a similar optimization
If no Route Reply is received, then larger TTL tried

## Slide 63: Summary: AODV
Routes need not be included in packet headers
Nodes maintain routing tables containing entries only for routes that are in active use
At most one next-hop per destination maintained at each node
  Multi-path extensions can be designed
  DSR may maintain several routes for a single destination
Unused routes expire even if topology does not change

## Slide 64: Proactive Protocols

## Slide 65: Proactive Protocols
Most of the schemes discussed so far are reactive
Proactive schemes based on distance-vector and link-state mechanisms have also been proposed

## Slide 66: Link State Routing [Huitema95]
Each node periodically floods status of its links
Each node re-broadcasts link state information received from its neighbor
Each node keeps track of link state information received from other nodes
Each node uses above information to determine next hop to each destination

## Slide 67: Optimized Link State Routing (OLSR) [Jacquet00ietf,Jacquet99Inria]
The overhead of flooding link state information is reduced by requiring fewer nodes to forward the information
A broadcast from node X is only forwarded by its multipoint relays
Multipoint relays of node X are its neighbors such that each two-hop neighbor of X is a one-hop neighbor of at least one multipoint relay of X
  Each node transmits its neighbor list in periodic beacons, so that all nodes can know their 2-hop neighbors, in order to choose the multipoint relays

## Slide 68: Optimized Link State Routing (OLSR)
Nodes C and E are multipoint relays of node A
A
B
F
C
D
E
H
G
K
J
Node that has broadcast state information from A

## Slide 69: Optimized Link State Routing (OLSR)
Nodes C and E forward information received from A
A
B
F
C
D
E
H
G
K
J
Node that has broadcast state information from A

## Slide 70: Optimized Link State Routing (OLSR)
Nodes E and K are multipoint relays for node H
Node K forwards information received from H
  E has already forwarded the same information once
A
B
F
C
D
E
H
G
K
J
Node that has broadcast state information from A

## Slide 71: OLSR
OLSR floods information through the multipoint relays
The flooded information itself is for links connecting nodes to respective multipoint relays
Routes used by OLSR only include multipoint relays as intermediate nodes

## Slide 72: Destination-Sequenced Distance-Vector (DSDV) [Perkins94Sigcomm]
Each node maintains a routing table which stores
  next hop towards each destination
  a cost metric for the path to each destination
  a destination sequence number that is created by the destination itself
  Sequence numbers used to avoid formation of loops
Each node periodically forwards the routing table to its neighbors
  Each node increments and appends its sequence number when sending its local routing table
  This sequence number will be attached to route entries created for this node

## Slide 73: Destination-Sequenced Distance-Vector (DSDV)
Assume that node X receives routing information from Y about a route to node Z
Let S(X) and S(Y) denote the destination sequence number for node Z as stored at node X, and as sent by node Y with its routing table to node X, respectively
X
Y
Z

## Slide 74: Destination-Sequenced Distance-Vector (DSDV)
Node X takes the following steps:
  If S(X) > S(Y), then X ignores the routing information received from Y
  If S(X) = S(Y), and cost of going through Y is smaller than the route known to X, then X sets Y as the next hop to Z
  If S(X) < S(Y), then X sets Y as the next hop to Z, and S(X) is updated to equal S(Y)
X
Y
Z

## Slide 75: Τέλος Ενότητας # 13
Μάθημα: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 13: Δρομολόγηση σε Κινητά Αδόμητα Δίκτυα (Mobile Ad Hoc Networks)
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής