## Slide 1: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 12: Mobile Transport Layer
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Congestion control in mobile & wireless networks
TCP assumes congestion if packets dropped  typically wrong in mobile & wireless networks
  Unchanged TCP performance degrades severely
Packet loss in mobile & wireless networks can be due to
  Wireless transmission errors
  Mobility when node moves from one network attachment point to another while there are still packets in transit

## Slide 3: Congestion control in mobile & wireless networks (cont.)
TCP reacts to packet loss with reduction of congestion window
Correct reaction when loss is due to link congestion
  Rate of packets entering a queue is larger than rate at which packets leave queue
May not be correct reaction when loss is due to wireless transmission errors:
  physical layer transmission rate should be reduced (or transmission power increased)

## Slide 4: TCP congestion control
  Congestion avoidance
Slow start
  Timeout after packet loss

## Slide 5: Solution
How to solve performance degradation of TCP over wireless
  Ideal TCP behavior: TCP retransmits packets lost due to wireless transmission errors without taking congestion control actions
  Ideal network behavior: hide transmission errors from TCP sender
    Includes avoiding errors and indirect effects such as increase of delay & delay variation
  Approaches try to achieve one of the above
    Ideal behavior cannot be realized in practise

## Slide 6: Alternative approaches
Link layer approach
  TCP-unaware and TCP-aware
Split connection approach
  Split end-to-end TCP connection
End-to-end approach
  Explicit notification schemes

## Slide 7: Link layer mechanisms
Forward Error Correction
  Corrects small number of errors
  Overhead incurred even when no errors occur
Link layer retransmission
  Overhead incurred only when errors occur
Above mechanisms are TCP-unaware

## Slide 8: Link layer retransmission issues
When to retransmit frame?
  Link layer retransmission timeout
  Negative acknowledgment
Maximum number of retransmissions?
  Finite or infinite
Retransmissions hide losses by influence end-to-end delay
  May have impact on TCP’s RTT estimation
Should link layer deliver packet in order or as they arrive?

## Slide 9: Link layer retransmission issues (cont.)
Can cause head of line blocking in sender queue
Can cause congestion losses (queue overflow)
Sender
Receiver 1
Receiver 2

## Slide 10: TCP-aware link layer
Snoop protocol, H. Balakrishnan et al. 1996
Transparent to TCP
  End-to-end semantics not changed
Buffers packets at access point to do local retransmission in case of packet loss

## Slide 11: TCP-aware link layer (cont.)
Access point
  snoops packets in both direction to identify acks
  buffers packets until ack identified
  retransmits packets in case of timeout or dupacks
Link layer retransmission

## Slide 12: TCP-aware link layer features
Access point maintains soft state
  Can recover if snoop agent crashes
Recovers errors only in direction from access point to mobile
Avoids retransmission at TCP sender by dropping dupacks from mobile
Cannot be applied if TCP data and acks traverse different path (asymmetric)
If RTT over wireless link small  simple (TCP-unaware) link layer retransmission performs equally well

## Slide 13: Split connection approach
Indirect TCP, B.R. Badrinath et al. 1995
End-to-end TCP connection broken into one connection over wired part and one over wireless part of path
  Two parts if there is one wireless link which is first or last hop
TCP over wireless link can be modified
  However, benefits can exist even with unmodified TCP due to smaller RTT

## Slide 14: Split connection approach (cont.)
Agent at access point acts as proxy
  Local retransmission in case of wireless losses
End-to-end semantics broken
  Ack at fixed TCP sender does not mean mobile received packet
  What happens if agent at access point crashes?
“wireless” TCP
Normal/wired TCP

## Slide 15: Split connection approach (contd.)
Access point maintains hard state
  Unlike Snoop approach where access point maintains soft state
Split connection allows independent congestion control over two parts
  Different congestion/error control protocols, timeouts, etc
Increased latency due to copying of packets across two connections

## Slide 16: Explicit notification schemes
Approximate ideal behavior: TCP should retransmits packet in case of errors without taking congestion control actions
TCP sender needs to know cause of loss
  wireless node identifies that loss is due to transmission error and notifies TCP sender
Variations
  Who sends explicit notification and when
  What sender does when notification received

## Slide 17: Explicit Loss Notification (ELN)
H. Balakrishnan et al. 1998
Mobile node is TCP sender
Access point tracks holes in packer sequent receiver from mobile sender
When dupack received from receiver, access point compares seq # with recorded holes
  In case of match sets ELN bit in dupack
If mobile sender receives dupack with ELN bit set: retransmits packet but does not reduce congestion window

## Slide 18: Observations
A lot of investigation and many techniques have been proposed
  Improvements for specific cases
Link layer retransmissions can improve performance without being TCP-aware
End-to-end techniques that do not require TCP specific support from lower layers, e.g. TCP Selective ACKnowledgements
Link layer techniques achieve higher gains compared to end-to-end schemes

## Slide 19: Impact of mobility on TCP
Handoff occurs when a mobile starts communicating with new base station (or foreign agent in case of mobile IP)
Link layer handoffs
  No change of IP address
  TCP will not be aware of handoff
  Link layer handles reliability
  Increased packet delay
Network layer handoff
  Need mobile IP
  Packets can be lost while mobile moves to new base station

## Slide 20: Improving TCP during mobility
Invoke fast retransmit after handoff
Buffer packets at base station (or foreign agent in case of mobile IP)
  Forward packets to new base station
Use multicast
  Send packets destined to mobile to current base station and base stations mobile is likely to visit next
  Incurs throughput & buffering overhead

## Slide 21: Τέλος Ενότητας # 12
Μάθημα: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 12: Mobile Transport Layer
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής