## Slide 1: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 6: Κυτταρική Δομή Κινητών Επικοινωνιών και Συστήματα Κινητής Τηλεφωνίας 1ης & 2ης Γενιάς
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Κυτταρική Δομή Κινητών Επικοινωνιών
Mobile Communications Principles
Early Mobile Telephone System Architecture
Co-channel Interference and Frequency Reuse
The Cellular Concept
Cellular System Architecture
Frequency Reuse
Cell Splitting
Handoff
Handoff Initiation
Cellular System Components
Digital Cellular
Time Division Multiple Access (TDMA)

## Slide 3: Mobile Communications Principles
each mobile (station)
  uses a separate, temporary radio channel to talk to the cell site
the cell site (base station)
  talks to many mobiles at once, using one channel per mobile
a pair of frequencies are used for communication
  one (the forward link) for transmitting from the cell site
  another frequency (the reverse link) for the cell site to receive calls from the users
mobiles must stay near the base station
  to maintain communications
  radio energy dissipates over distance
mobile (voice) networks include
  mobile radio service
    operates in a closed network
    no access to the telephone system
  mobile telephone service
    interconnection to the telephone
    network

## Slide 4: Early Mobile Telephone System Architecture































Traditional mobile service
  structured in a fashion similar to TV broadcasting
  one powerful transmitter in a (e.g.,metropolitan) area
    could broadcast in a radius of up to 50km
The cellular concept
  different!
  many low-power transmitters placed throughout an area

## Slide 5: Co-channel Interference and Frequency Reuse
co-channel interference
  caused by mobile units using the same channel in adjacent areas
  all channels cannot be (re-)used in every cell
  areas have to be skipped before the same channel is reused
frequency reuse is still a key technique for mobile communications systems
interference
  is not proportional to the distance between areas, but to the ratio of the distance between areas to the transmitter power (radius) of the areas
  reducing the radius of an area by 50%, increases the number of potential customers in an area 4x
    systems with a 1 Km radius can have 100 times more channels than systems with areas 10 Km in radius

## Slide 6: The Cellular Concept
variable low-power transmission levels
  allow cells to be sized according to
    subscriber density
    traffic demands
as the population or traffic grows
  cells can be added to accommodate that growth
frequencies used in one cell cluster can be re-used in other clusters
conversations can be handed-off from cell to cell
  to maintain continuous service as the user moves between cells
the base station can communicate with mobiles as long as they are within range
































## Slide 7: Cellular System Architecture
engineering plan
  clusters
  frequency reuse
  handovers
cells
  basic geographic unit of a cellular system
  base stations transmit over small geographic areas
  often represented as hexagons
  true shape of cells is not a perfect hexagon
    because of constraints imposed by
      natural terrain
      man-made structures
  cell size varies depending on the landscape
clusters
  a group of cells
  no channels are reused within a cluster

## Slide 8: Frequency Reuse
no channels are reused within a cluster
cells with same number have same group of frequencies
  they are far enough so that there is no interference
number of available frequency groups is 7
  frequency reuse factor=7
  each cell is using 1/7 of available channels
Hexagon cell pattern, values of N=1,3,7,9,12,13,16,19,21

## Slide 9: Reuse patterns
A
F
E
D
B
G
C
A
F
E
D
B
G
C
N = 7
A
B
C
B
B
C
C
C
B
B
A
C
A
A
A
N = 3

## Slide 10: Cellular architecture
Cellular backhaul or Radio Access Network: interconnect base stations to backbone
Can be wired or wireless (point-to-point)

## Slide 11: Increasing cellular capacity
Cell splitting
  smaller cells in high demand areas
  smaller cells => more base stations & more frequent handoffs
  smaller cells (micro cells) => reduced transmission power
Frequency borrowing
  congested cells borrow frequencies from less congested cells
  dynamic allocation of frequencies
Sectorization
  cell divided into sectors (typically 2-6)
  use directional (sector) antennas
3-sector cell

## Slide 12: Cell Splitting
creating full systems with many small areas impractical
cell splitting
  as a service area becomes full of users
  split a single area into smaller ones
urban centers
  can be split into as many areas as necessary
  to provide acceptable service levels in heavy-traffic regions
rural regions
  larger, less expensive cells

## Slide 13: Handoff
mobile subscriber travels from one cell to another during a call
  adjacent cells do not use the same radio channels
  call must either
    be dropped or
    transferred
    from one radio channel to another when a user crosses cells
  dropping the call is unacceptable
hand-off (US, hand-over in UK)
  mobile telephone network automatically transfers a call
  from radio channel to radio channel, as a mobile crosses adjacent cells

## Slide 14: Handoff Initiation
when MS moves out of the coverage area of a given cell site
  the reception becomes weak
  the cell site (in use) or the MS requests a handoff
  system switches the call to
    a new site (and channel) with
    a stronger signal
  without interrupting the call or alerting the user
  call continues as long as the user is talking, and the user does not notice the handoff at all

## Slide 15: Cellular System Components
public switched telephone network (PSTN)
mobile telephone switching office (MTSO)
cell site with antenna system
mobile subscriber unit (MSU)

## Slide 16: Cellular System Component Definitions
PSTN (public switched telephone network)
  made up of:
    local networks
    the exchange area networks, and
    the long-haul network (on a worldwide basis)
Mobile Telephone Switching Office (MTSO)
  the central office for mobile switching
  houses the mobile switching center (MSC), field monitoring, and relay stations for switching calls from cell sites to wireline central offices (PSTN)
  in analog cellular networks, the MSC controls the system operation:
  controls calls, tracks billing information, and locates cellular subscribers
the Cell Site
  refers to the physical location of radio equipment (providing coverage within a cell)
  includes:
    power sources
    interface equipment
    radio frequency transmitters and receivers, and
    antenna systems

## Slide 17: Συστήματα Κινητής Τηλεφωνίας 1ης & 2ης Γενιάς
1st generation
  AMPS
2nd generation
  GSM
  DAPMS, IS-54, IS-136 (TDMA)
    CDPD (Packet Data extension)
  IS-95 (CDMA)

## Slide 18: North American Analog Cellular Systems
originally devised in the late 1970s to early 1980s
operate in the 800-MHz range
system development takes into consideration many different, and often opposing, requirements
  often a compromise between conflicting requirements results
cellular development involves the following basic topics:
  frequency and channel assignments
  type of radio modulation and modulation parameters
  maximum power levels
  messaging protocols
  call-processing sequences

## Slide 19: AMPS: Advanced Mobile Phone Service
U.S. (’80s)
Analog
cell size: 1km2 … 100km2
indoor coverage: problematic
































## Slide 20: Advanced Mobile Phone Service (AMPS)
released in 1983
a fully automated mobile telephone service
the first standardized cellular service in the world
used throughout the world
    United States
    South America
    China
    Australia
designed for use in cities, later expanded to rural areas
maximized the cellular concept of frequency reuse
  by reducing radio power output
AMPS telephones (or handsets)
  have the familiar telephone-style user interface
  are compatible with any AMPS base station
mobility between service providers (roaming) possible

## Slide 21: AMPS (cont.)
using the 800-MHz to 900-MHz frequency band
30-kHz bandwidth for each channel
frequency modulation (FM) for radio transmission
in the US, Frequency Division Duplex (FDD):
  separate frequencies for
    transmissions from mobile to base station
    transmissions from the base station to the mobile subscriber
  (alternative to FDD is Time Division Duplex--TDD)

## Slide 22: AMPS Limitations
low calling capacity
limited spectrum
no room for spectrum growth
poor data communications
minimal privacy
inadequate fraud protection

## Slide 23: Narrowband Analog Mobile Phone Service (NAMPS)
introduced as an interim solution to AMPS capacity problems
operational in 35 U.S. and overseas markets
combines
  existing voice processing
  with digital signaling
tripling the capacity of today's AMPS systems
3 channels from a single AMPS 30-kHz channel
  FDM
  provides 3 users in an AMPS channel
increased probability of interference
  thus lower voice quality
  because channel bandwidth is reduced for a call (compared to AMPS)

## Slide 24: Συστήματα Κινητής Τηλεφωνίας 2ης Γενιάς
GSM (discussed extensively later)
TDMA (IS-54, then IS-136)
CDMA (IS-95)
  “marketing name” PCS (IS-95 based)
    smaller cells, higher speeds

## Slide 25: AMPS/DAMPS Comparison

## Slide 26: CDPD: Cellular Digital Packet Data
CDPD: data (IP) on AMPS (extended)
AMPS: U.S. (’80s)
  Analog
  cell size: 1km2 … 100km2
  modems for data (error control)
    20-30 s set-up
    up to 4.8 Kb/s
CDPD
  exploiting 30+% idle time on AMPS circuit-switching channels
  40 ms delay for voice to recapture channel
  channel hopping
  up to 19.2 Kb/s
  IP

## Slide 27: GSM - Global System Mobile
European, introduced in 1992
digital cellular, TDMA based
extended for data traffic at 9.6 Kb/s
short messages (160 Bytes)
frequencies
  900 Mhz, 1800 Mhz (DCS), in Europe
  1900 Mhz in the U.S.
































## Slide 28: Τέλος Ενότητας # 6
Μάθημα: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 6: Συστήματα Κινητής Τηλεφωνίας1ης & 2ης Γενιάς
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής