## Slide 1: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 7: Σύστημα Κινητής Τηλεφωνίας GSM
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: GSM frequency bands (common)
GSM: Global System for Mobile Communications
GSM-900 and GSM-1800
  Europe, Middle East, Africa, most of Asia
GSM-850 and GSM-1900
  USA, Canada, other countries in America
GSM-400 and GSM-450 rarer

## Slide 3: Network architecture

## Slide 4: Network elements
Mobile Station
  Mobile Equipment
    Identified by the International Mobile Equipment Identity (IMEI)
  Subscriber Identity Module (SIM)
    Contains a unique identification number called IMSI
    It is removable, thus irrespective of a specific terminal

## Slide 5: Base Station Subsystens
Base Station Subsystem (BSS)
  Base Transceiver Station (BTS)
    A BTS is comprised of radio transceivers, antennas, the interface to the PCM facility
    BTS is the entity that connects the mobiles to a cellular network
  Base Station Controller (BSC)
    Its primary function is call maintenance, by deciding when to initiate a handover, changing the BTS transmitter power, etc.
    A BSC is connected to a group of BTSs and manages the radio resources for them

## Slide 6: Network Subsystem
Network Subsystem
  Mobile Switching Center (MSC)
    MSC provides functions such as registration, authentication, location updating, handovers and call routing to a roaming subscriber
  Home Location Register (HLR)
    The HLR contains all the administrative information and current location of each subscriber registered in the corresponding GSM network
  Visitor Location Register (VLR)
    Contains subscription information needed for call control, for all mobiles in the area of the associated MSC
  Equipment Identity Register (EIR)
    EIR is a database that contains a list of all valid mobile equipment on the network
  Authentication Center (AUC)
    Stores the secret key held in each user’s SIM card

## Slide 7: Application Service Centers
Application Service Centers are responsible for GSM network add-on services
  Operation and Maintenance Center (OMC)
    Monitoring and control the network
    Usually connect with MSC, BSC, HLR, and other service centers
  Short Message Service Center (SMSC)
    provide short message services
    usually connect to MSC
  Unstructured Supplementary Service Data Center (USSDC)
    provide USSD service in the form of *ID*ID*info#
    usually connect to HLR

## Slide 8: GSM functional planes
mobility and security,
HLR and VLR
stable radio connections, handover
coding, modulation, mux
call control

## Slide 9: Protocol stack

## Slide 10: GSM FDMA
25 MHz
25 MHz
Mobile to Base
0
1
2
890.2
890.4
890.6
(MHz)
Base to Mobile
0
1
2
935.2
935.4
935.6
200 kHz
45MHz
Channel layout and frequency bands of operation
890
935
960
915
200 kHz

## Slide 11: GSM TDMA
8
7
6
5
4
3
2
1
8
7
6
5
4
3
2
1
45 MHz
Frequency
F2’
F1’
(Cell Tx)
F2
F1
(Cell Rx)
Amplitude
Typical TDMA/ FDMA frame structure

## Slide 12: GSM FDMA/TDMA

## Slide 13: GSM channels
Physical channel: specific time slot and channel/carrier frequency
Logical channels
  run over physical channels (not necessarily in all time slots)
  two types: traffic and control
  managed: setup, maintenance, tear-down
Control channels interspersed with traffic channels in well-defined ways

## Slide 14: GSM logical channels
TCH: traffic
  full-rate
  half-rate
BCH: εκπομπής προς όλους
CCCH: ελέγχου, κοινό
DCCH: ελέγχου, ιδιαίτερο
ACCH: ελέγχου, σχετιζόμενο

## Slide 15: GSM logical channels (cont.)

## Slide 16: Traffic channels
Full rate: 22.8 kbps
  speech data: 13 kbps voice data + FEC
  packet data: 12,6,3.6 kbps + FEC
Half rate: 11.4 kbps
To achieve higher rates multiple logical channels have to be allocated (GPRS does this)

## Slide 17: Control channels
Help MS locate control channels
Provide information about
  voice and control channel repetition cycle.
  parameters in the cell
  surrounding cells
  paging
Allow random access attempts by the MS

## Slide 18: Broadcast Control Channels
FCCH (Frequency Correction Channel)
  carrier synchronization
  base station “beacon” signal
SCH (Synchronization Channel)
  frame synchronization
BCCH (Broadcast Control Channel)
  cell ID, available services, etc

## Slide 19: Common Control Channels
PCH (Paging Channel) - downlink
  page a mobile
AGCH (Access Grant Channel) - downlink
  reply to a random access request, assign dedicated control channel
RACH (Random Access Channel) – uplink
  used by mobile to request dedicated control channel
  messages from several mobiles can collide
  Slotted Aloha used for contention resolution

## Slide 20: Dedicated and Control Channels
SACCH (Slow Associated Control Channel)
  in-band signaling
  downlink: system info, power control
  uplink: measurements
FACCH (Fast Associated Control Channel)
  in-band time-critical signaling
  call establishment progress, authentication, handover signaling
SDCCH (Stand-alone Dedicated Control Channel)
  out-of-band signaling
  call setup signaling, SMS, location update

## Slide 21: Mobile initialization

## Slide 22: Location update

## Slide 23: Call origination (MS->BSS)

## Slide 24: Call termination (BSS->MS)

## Slide 25: GSM identifiers
IMSI: non-dialable number
  MCC Greece: 202
  Bound to SIM
TMSI: Temporary MSI (confidentiality)
MS ISDN number (dialable)
  Different MS ISDN can be associated to same SIM

## Slide 26: Call routing
IMSI: International Mobile Subscriber Identifier
MSISDN: MS ISDN (called number)
MSRN: Mobile Station Routing Number

## Slide 27: Mobility management
Location Registration
Call delivery
Handoff Management
  Handoff is caused by:
    signal strength deterioration
    user mobility
  There are two kinds of handoff:
    soft handoff
    hard handoff
  There are three ways to handoff:
    network-controlled handoff
    mobile-assisted handoff
    mobile-controlled handoff
Rx
signal strength

## Slide 28: Three cases of handovers

## Slide 29: Power control
Operator - dependent
Mobile:
  Peak Tx power classes: GSM-900: 8,5,2,0.8 Watt (39,37,33,29 dBm), GSM-1800: 1,0.25,4 Watt (30,24,36 dBm)
  minimum Tx power: GSM-900: 19mW, GSM-1800: 15mW
  step: 2dBm
Base station:
  8 classes: 320-2.5 Watt (55-34dBm)
Base station decides power control changes for both
  Mobile measures signal strength, quality (BER) and reports to Base station
  Goal: operate at lowest power level while maintaining acceptable signal quality

## Slide 30: Τέλος Ενότητας # 7
Μάθημα: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 7: Σύστημα Κινητής Τηλεφωνίας GSM
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής