## Slide 1: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 14: Ασύρματα Δίκτυα Πλέγματος (Wireless Mesh Networks)
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες: Ασύρματα Δίκτυα Πλέγματος (Wireless Mesh Networks)
Χειμερινό Εξάμηνο 2015-16
Βασίλειος Σύρης
Οικονομικό Πανεπιστήμιο Αθηνών
Τμήμα Πληροφορικής

## Slide 3: Infrastructure vs. infrastructure-less networks
Cellular, WLANs
  rely on infrastructure (=planning)
Ad hoc networks
  no infrastructure
  no connection to fixed network
Wireless mesh networks
  wireless multi-hop
  have connection to fixed network

## Slide 4: Wireless Mesh Networks (WMNs)
What are they?
  multi-hop wireless networks
  typically mesh nodes are stationary
  mesh nodes have multiple radios
  mesh networks are connected to a wired network
Why are they interesting?
  extend reach of wired networks
  provide access to fixed/nomadic/mobile users
  reduced deployment time and operation costs
differences with
MANETs (Mobile Ad Hoc Networks)

## Slide 5: MANET

## Slide 6: Wireless Mesh Network

## Slide 7: MANETs vs. WMNs
Mobile Ad Hoc Networks (MANETs)
user devices are also intermediate nodes (perform forwarding)
both end and intermediate nodes are mobile
no connection to fixed network
connectivity primary issue
devices have single wireless interface
Wireless Mesh Networks (WMNs)
only intermediate mesh nodes only perform forwarding
only end-user devices are mobile; mesh nodes are fixed
one or more connections to fixed network
reliability, throughput, and delay important
devices can have multiple wireless interfaces

## Slide 8: Wireless Embedded and Sensor Networks
embedded device: a device with a computer, which are not a computer themselves
embedded wireless device: a device with a wireless interface built in
Features
  both sensing and actuation
  interact with environment and people
  constrained resources (processing, power, storage)
WSNs: isolated
WENs: connected to Internet
  renewed interest in IPv6-based

## Slide 9: WMNs as Access Networks
Wireless mesh network provides access to virtual capacity pool
Virtual capacity pool aggregates capacity from many subscriber & provider links
Access for stationary and mobile users
Support for QoS, dependability, and security
virtual capacity pool
WMN

## Slide 10: Neighborhood/Community Mesh
Notes:   Home residence: a user uploads a video taking advantage of the aggregated bandwidth

## Slide 11: Emergency Mesh
Notes: Ephemeral: deployment for ad-hoc events, such as an exhibition or an emergency situation

## Slide 12: Metropolitan Mesh
Notes: Metropolitan: augment already existing wireline infrastructure to bring bandwidth to public areas, or deploy a completely wireless solution (Ozone)

## Slide 13: Rural Mesh Network
Directional links
Omni-directional links
City

## Slide 14: Heraklion Metropolitan MESH Test-bed
60 Km2 coverage
14 nodes, 5 core multi-radio nodes
1.6 – 5 Km links
Antennas: 19/21/26 dBi panel
Three fixed network connections (FORTH & UoC)
Independent mgmt / monitoring network

## Slide 15: Multi-radio mesh node
Mini-ITX board (EPIA SP 13000, 1.3 GHz C3, 512 MB ram)
Four mini PCI Atheros-based 802.11a/g wireless cards
Gentoo 2006 i686 Linux (2.6.18), MadWiFi version 0.9.2
OLSR deamon version 0.4.10
Independent 802.11a client for management/monitoring
Intelligent remote power switch
Ethernet switch
to antenna
power in
remote
power switch
mini ITX
802.11
client
HDD
to four antennas
Component layout
Actual node

## Slide 16: Actual deployment pictures

## Slide 17: Channel assignment
Channel assignment can control topology
Two nodes can communicate when they have at least one interface in common channel
1 channel
1 interface
4 channels
2 interfaces
A
D
B
C
A
B
C
D
A
B
C
D
3 channels
2 interfaces

## Slide 18: Channel assignment (cont.)
Similar to a graph coloring problem, except that
  We are given some number of colors (channels)
  We are looking for coloring with least conflicts
Need to model interference
Channel assignment can be addressed jointly with routing

## Slide 19: Signal propagation range
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible
Interference range
  signal may not be detected
  signal adds to the background noise
distance
transmission
detection
interference
sender

## Slide 20: Modeling interference
Conflict graph: vertices are links between nodes
Multi-radio nodes with directional antennas: not all interfaces equivalent
3-node network
conflict graph

## Slide 21: Routing in WMNs
Contention can be both intra-flow and inter-flow
Contention level depends on # of flows and transmission rate
A
B
C
A
B
C
D
E
CH 1
CH 1
CH 1
CH 2
CH 2
intra-flow
inter-flow

## Slide 22: Τέλος Ενότητας # 14
Μάθημα: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 14: Ασύρματα Δίκτυα Πλέγματος (Wireless Mesh Networks)
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής