## Slide 1: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 4: Πρωτόκολλα Πολλαπλής Προσπέλασης
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Multiple access
Goal: share a common communication medium among multiple transmitting nodes
Objectives/issues:
  High resource utilization
  Avoid starvation (fairness)
  Simplicity

## Slide 3: Switching
Circuit switched-based
Packet-based
  Datagram switching
  Virtual circuit switching

## Slide 4: Multiple access
Fixed assignment
FDM,
TDM,
CDM,
centralized
Aloha, CSMA,
CSMA/CA
Contention-less
Contention-based
Random access
Random access with reservation
Polling
Token passing
Cellular, satellite

## Slide 5: Multi-Access Radio Techniques
Courtesy of Petri Possi, UMTS World

## Slide 6: CDMA

## Slide 7: Frequency hopping
Frequency hopping based on pseudorandom numbers
Spreads power over wide spectrum: spread spectrum
Narrowband interference not effective
Initially developed for military

## Slide 8: Direct sequence
Spreading factor: code bit rate/data bit rate
  10-100 typically for commercial systems
Signal bandwidth = Spreading factor X Data rate
Code sequence synchronization necessary
Correlation between codes => interference

## Slide 9: OFDMA
Orthogonal Frequency Division Multiple Access
Multicarrier modulation similar to DMT
Available frequency band divided into many (256 or more) sub-bands
Orthogonal: peak of one band at null of others
Each carrier modulated with BPSK, QPSK, 16/64-QAM, etc

## Slide 10: Wideband CDMA
Bandwidth >= 5MHz
Multirate: variable spreading and multicode
Power control:
  open power control
  fast closed-loop power control
Frame length: 10ms/20ms (optional)

## Slide 11: Multiple Access Systems
Nodes use common transmission channel
Collisions when two or more hosts send simultaneously
Access Control design problem: limit inefficiencies due to collisions and idle periods
…

## Slide 12: Multiple Access Control
TDM: inefficient
Ethernet: based on CSMA/CD (Carrier Sense Multiple Access/ Collision Detect
  Wait for idle channel, then send packet
  Stop if collision detected
  Wait for random delay after collision
ALOHA: less polite than Ethernet
  Transmit whenever packet is ready
  Stop if collision detected
  Wait for random delay after collision

## Slide 13: Multiple Access Control (cont)
Token passing
  Token passed from one node to another
  Node transmits if it has token
  Need to make sure token not lost, and no one node exhibits unfair behavior
Token ring: nodes connected in ring topology

## Slide 14: OSI and IEEE 802

## Slide 15: IEEE 802 Layers - Physical
Encoding/decoding
Preamble generation/removal
Bit transmission/reception
Transmission medium and topology

## Slide 16: IEEE 802 Layers - Logical Link Control (LLC)
Interface to higher levels
Multiplexing
Flow and error control

## Slide 17: IEEE 802 Layers - Media Access Control (MAC)
Assembly of data into frame with address and error detection fields
Disassembly of frame
  Address recognition
  Error detection
Govern access to transmission medium
  Not found in traditional layer 2 data link control
For the same LLC, several MAC options may be available
Examples:
  802.3 (Ethernet)
  802.4 (Token Bus)
  802.5 (Token Ring)
  802.11 (Wireless LAN, Wi-Fi, or wireless Ethernet)
  802.15 (Bluetooth)
  802.16 (Wireless Local Loop – WLL)

## Slide 18: Media Access Control (MAC)
Goal: share a communication medium among multiple hosts connected to it
Objectives/issues:
  High resource utilization
  Avoid starvation (fairness)
  Simplicity
Solutions:
  Centralized
    + Greater control, simple access logic and co-ordination
    - Single point of failure, potential bottleneck
  Distributed: random access, taking turns
  On demand or synchronous

## Slide 19: MAC Protocol: A Taxonomy
Channel partitioning
  Divide channel into smaller “pieces” (time slots, frequency)
  Allocate piece to node for exclusive use
Random access
  Allow collisions
  “recover” from collisions
“Taking-turns”
  Tightly coordinate shared access to avoid collisions
  Token ring, toke bus

## Slide 20: Random Access MAC Protocols
Stations access medium randomly
Collisions when two or more hosts send simultaneously
Random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions
Access Control design problem: limit inefficiencies due to collisions and idle periods
Examples:
  ALOHA (Slotted, Pure)
  CSMA and CSMA/CD (Ethernet)
  CSMA/CA (Wireless LAN/ IEEE 802.11)

## Slide 21: Random Access MAC Protocols: Performance
Efficiency=maximum fraction of time nodes transmit packets successfully
Throughput=maximum rate of successful bit transmission = (Efficiency)  (Transmission rate)

## Slide 22: ALOHA Protocol
ALOHA: packet-switched radio communication network
  University of Hawaii, 1970s
  Can also run over wired media (coaxial cable, twisted pair)
Father of multiple access protocols
Transmission rate of original ALOHA network : 9600 bps
Two versions: Slotted and Pure

## Slide 23: Slotted ALOHA
Time is divided into equal size slots (= packet transmission time)
Node with new pkt: transmit at beginning of next slot
If collision: retransmit pkt in future slots after random delay (why random?)
Success (S), Collision (C), Empty (E) slots

## Slide 24: Slotted ALOHA
Time in uniform slots equal to frame transmission time
  All frame (packets) have fixed size
Need central clock (or other sync mechanism)
Transmission begins at slot boundary
Sender (wireless stations):
  Waits for ACK after packet transmission
  Retransmits frame after Timeout
Receiver (base station):
  Error detection using Frame Check Sequence (similar to CRC)
  Send ACK if frame OK
Max utilization 36%

## Slide 25: Slotted ALOHA Transmissions
Frames either miss or overlap totally
Wasted time:
  Slots with collisions
  Unused slots

## Slide 26: Slotted ALOHA: Efficiency
G: total rate of transmission attempts (pkts/timeslots)
S: rate of successful transmissions (pkts/timeslots)
p: probability of successful packet transmission
Assumptions:
  Infinite number of stations
  Number of packet arrivals is Poisson distributed
From above

## Slide 27: Slotted ALOHA: Efficiency (cont)
Hence
S  1/e  36%
What if there are only two stations?

## Slide 28: Slotted ALOHA: Finite Station Population
Finite number of stations N
  Each transmits in slot with probability q
Probability of successful transmission
  Above is maximized for q=1/N
  A node does not know number N of other stations that have packet to transmit
Single station:
N stations:

## Slide 29: Slotted ALOHA: Finite Station Population (cont)
Maximum efficiency for finite population ALOHA

## Slide 30: Pure ALOHA
No slotted time as in pure ALOHA
When station has frame, it sends
Any overlap of frames causes collision

## Slide 31: Pure ALOHA: Performance
Probability of successful packet transmission
Hence

## Slide 32: Reservation ALOHA
Two phases:
  Reservation phase
  Transmission phase
Reservation phase: Slotted ALOHA
Transmission phase:
  Divided into time slots
  Station to transmit in each time slot determined by reservations
  Duration of transmission phase depends on # of successful reservations
…
Reservation
phase
Transmission
phase
Reservation
phase
Transmission
phase

## Slide 33: Reservation ALOHA: Efficiency
Reservation phase is slotted ALOHA: 36% efficiency
Transmission phase: 100% efficiency
TRES: size of reservation slot
TRANSP: size of transmission slot
Average duration of reservation: TRES/0.36
Example: TRES/TRANSP=1/20

## Slide 34: Carrier Sense Multiple Access (CSMA)
Carrier Sense: “Listen before talking”
Sender:
  Listen for clear medium (carrier sense)
  If medium idle
    Transmit whole frame
    Start Timeout and wait for ACK
  If medium busy
    Defer transmission -> Three alternatives
Receiver:
  Send ACK if packet received correctly

## Slide 35: Why ALOHA doesn’t listen…
ALOHA targeted for wide area and satellite systems
  These have long propagation delays
  “Send and pray” is about the best you can do for random access
ALOHA not a good choice for local area networks
  These have short propagation delays

## Slide 36: CSMA: What happens if channel is busy?
1-persistent CSMA:
  Continue listening for idle channel
  When channel becomes idle transmit whole packet immediately
p-persistent CSMA:
  Continue listening for idle channel
  When channel becomes idle transmit packet with probability p
  Assumes slotted time (like slotted ALOHA)
Non-persistent CSMA:
  When channel busy, wait for random time, then check channel again

## Slide 37: CSMA persistence schemes
1-persistent:
  If two or more stations waiting to transmit, collision is guaranteed
Non-persistent:
  Reduces probability of collisions
  Wasted idle time before transmissions
p-persistent:
  How is p selected ? Must be Np<1
  Np>1 instability, Np<<1 unnecessarily long delays
Constant or variable delay
Non-persistent
Channel busy
Sense channel
p-persistent
1-persistent

## Slide 38: CSMA: efficiency
PROP/TRANSP=0.1
P.ALOHA
S.ALOHA
non-persistent CSMA
1-p CSMA
G, offered traffic
efficiency

## Slide 39: CSMA Collisions
Collisions can occur:
propagation delay means
two nodes may not
hear each other’s transmission
Collision:
entire packet transmission
time wasted
spatial layout of nodes along ethernet

## Slide 40: CSMA/CD (Collision Detect)
Collision Detect: listen while transmitting
CSMA/CD steps
If medium idle, transmit
If busy, listen for idle, then transmit (1-persistent)
If collision detected, jam then cease transmission
After jam, wait random time then start again
  Binary exponential back off

## Slide 41: Collision Detection
Easy in wired LANs: measure signal strengths, compare transmitted, received signals
Difficult in wireless LANs
  receiver shut off while transmitting
  one station cannot hear all other stations

## Slide 42: Gains of Collision Detect

## Slide 43: Maximum Time to Detect Collision
T2-T1=T4-T3=PROP
Minimum time to detect collision: T4-T1=2PROP
Minimum frame length: TRANSP > 2PROP
A
B
Time T1
Time T2
B starts transmission just prior
to signal A reaching it
Time T3
B senses collision, stops transmitting and sends jam signal
Time T4
A transmission
Bus signal
A transmission
Bus signal
A transmission
Bus signal
collision
A transmission
Bus signal
collision

## Slide 44: CSMA/CD Efficiency
P.ALOHA
S.ALOHA
non-persistent CSMA
1-p CSMA
CSMA/CD
PROP/TRANSP=0.1
G, offered traffic
efficiency

## Slide 45: Τέλος Ενότητας # 4
Μάθημα: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 4: Πρωτόκολλα Πολλαπλής Προσπέλασης
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής