## Slide 1: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 3: Ασύρματο Κανάλι και Διάδοση Σημάτων
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: What is wireless networking
Any form of communication that does not require the transmitter and receiver to be in physical contact
Simplex: one-way communication (e.g., radio, TV)
Half-duplex: two-way communication but not simultaneous (e.g., walkie-talkie, CB)
Full-duplex: two-way communication (e.g., cellular phones)

## Slide 3: Basic communication system (single hop)
Transmitter performs encoding, modulation, and multiplexing
Receiver performs demodulation and demultiplexing
Channel
Transmitter
(Tx)
Receiver
(Rx)

## Slide 4: Basic communication network (multiple hops)
Wired communication: channels independent (no interference)
Wireless: channels interfere
Same feature can be an advantage: broadcast
Tx/Rx
Node
Channel
Channel
Tx/Rx
Channel
Channel

## Slide 5: Basic wireless terms
Frequency
Spectrum
Bandwidth
Capacity

## Slide 6: Frequency
Frequency is the number of times that a wave's peak passes a fixed point in a specific period of time
Point A
10 Cycles / 1 Second = 10 Hertz
1 Second

## Slide 7: Frequency (cont)
Frequency is measured in cycles per second, or Hertz (Hz)
Cellular phones, for example, produce radio waves with frequencies around 900 million Hz (900 MHz)
  1,000 Hz = 1 KiloHertz (kHz)
  1,000,000 Hz = 1 MegaHertz (MHz)
  1,000,000,000 Hz = 1 GigaHertz (GHz)

## Slide 8: Spectrum
For our purposes, spectrum is the term that describes a set of radio waves that can be used to transmit information

## Slide 9: Electromagnetic spectrum
Wireless communications: 100KHz-60GHz

## Slide 10: Wireless Spectrum (1)
30 MHz
30 GHz
3 GHz
300 MHz
Broadcast TV
VHF: 54 to 88 MHz, 174 to 216 MHz
UHF: 470 to 806 MHz
FM Radio
88 to 108 MHz
Digital TV
54 to 88 MHz, 174 to 216 MHz, 470 to 806 MHz

## Slide 11: Wireless Spectrum (2)
30 MHz
30 GHz
3 GHz
300 MHz
3G Broadband Wireless
746-794 MHz, 1.7-1.85 GHz, 2.5-2.7 GHz
Cellular Phone
800-900 MHz
Personal Communication Service (PCS)
1.85-1.99 GHz

## Slide 12: Wireless Spectrum (3)
Local Multipoint Distribution Services (LMDS)
27.5-31.3 GHz
30 MHz
30 GHz
3 GHz
300 MHz
Wireless LAN (IEEE 802.11b/g)
2.4 GHz
Bluetooth
2.45 GHz
Wireless LAN (IEEE 802.11a)
5 GHz

## Slide 13: ISM Band (Industrial Scientific Medical)
Unlicensed
Used mainly by WLANs

## Slide 14: Basic properties
Moving from left to right
  higher bandwidth
  shorter range (higher attenuation, blocking)
  more power
  more sophisticated electronics

## Slide 15: Radio Spectrum Allocation (USA)

## Slide 16: Frequency vs. Bandwidth
Frequency is a specific location on the electromagnetic spectrum
Bandwidth is the range between two frequencies
  Bandwidth is measured in Hertz
  A cellular operator may transmit signals between 924-949 MHz, for a total bandwidth of 25 MHz

## Slide 17: Bandwidth vs. Capacity
Bandwidth for a particular service is fixed, but the number of calls and the rate of data transmission is not (capacity)
The technology used determines the capacity of a particular bandwidth
Shannon capacity fundamental limit

## Slide 18: Signal strength (or power)
The ability of an electromagnetic wave to persist as it radiates out from its transmitter
Signal strength, or power, is measured in Watts, or more conveniently expressed relative to milliWatts in decibels (dBm)

## Slide 19: Signal propagation range
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible
Interference range
  signal may not be detected
  signal adds to the background noise
distance
transmission
detection
interference
sender

## Slide 20: Fading
Large-scale fading
Small-scale fading
Flat (frequency non-selective) fading

## Slide 21: Fading (1)
path loss
slow fading (also called long term, shadowing)
fast fading (short term)
With path loss, shadow
fading, and Rayleigh fading
With path loss
log (distance)
Received
Signal
Power
(dB)
With path loss and
shadow fading

## Slide 22: Fading (2)
fading due to multipath and mobility
dB With Respect
to Average Value
0
0.5
0.5l
1.5
-30
-20
-10
10
0
1
t, in seconds
0
10
30
20
x, in wavelength
Received
Signal
Power
(dB)

## Slide 23: Multipath

## Slide 24: Multipath and delay spread
Delay spread: time between first and last version of signal
Multipath may add constructively or destructively => fast fading

## Slide 25: Free space propagation model
Power of wireless transmission reduces with square of distance (due to surface area increase)
Reduction also depends on wavelength
  High wavelength/low frequency has less loss
  Small wavelength/high frequency has more loss

## Slide 26: Fading (cont)
path loss
slow fading (also called long term, shadowing)
fast fading (short term)
With path loss, shadow
fading, and Rayleigh fading
With path loss
log (distance)
Received
Signal
Power
(dBm)
With path loss and
shadow fading

## Slide 27: General propagation model
PL0 loss at reference distance d0
Path loss exponent a depends on environment
  Free space 2
  Urban area cellular 2.7 to 3.5
  Shadowed urban cell 3 to 5
  In building LOS 1.6 to 1.8
  Obstructed in building 4 to 6
  Obstructed in factories 2 to 3

## Slide 28: dB and dBm
Decibel (dB): relative unit of measurement
Signal strength or power measured in dBm: power relative to 1mW
  1mW = 0dBm
  100mW=20dBm
  200mW=23dBm
  1000mW=30dBm

## Slide 29: Path loss in dB
Path loss when power measured in Watt
Path loss when power measured in dBm
3dB loss = power halved (3dB  10log2)
easier to do addition/subtraction compared to multiplication/division

## Slide 30: General propagation model (cont)
PL0 loss at reference distance d0
in dB
  path loss increases linear to log of distance

## Slide 31: Path loss in different environments

## Slide 32: Antenna radiation
Isotropic antenna (idealized) radiates power equally in all directions
Most practical antennas do not radiate power equally in all directions
  antenna’s radiation pattern shows energy it transmits/collects in each direction
Antenna gain measured in dBi
  power output in preferred direction compared to perfect isotropic antenna

## Slide 33: Antenna gain

## Slide 34: Antenna types
Isotropic antenna (idealized)
  Radiates power equally in all directions
Omni-directional
Dipole antennas
Yagi
Parabolic or dish
Sector
Panel

## Slide 35: Omni-directional antennas
Indoor and outdoor
Typically 2-15 dBi

## Slide 36: Yagi
referred to as Yagi – Uda
typically very directional
Cantenna: built from Pringles box!

## Slide 37: Parabolic
grid/wiretype or satellite dish (solid)

## Slide 38: Sector and panel antennas
Patch: smaller version of panel antenna

## Slide 39: Antenna radiation patterns
Omni
Parabolic
Dipole
Yagi
Patch
Sector

## Slide 40: EIRP
EIRP: Effective Isotropic Radiated Power
EIRP=Transmitter Power + Transmitter Gain – Cable Loss
European Radiocommunications Committee (ERC) sets max average EIRP (FCC in US)
max EIRP
  2.4GHz: max EIRP=100mW (20dBm)
    US: 36 dBm (9dBi omni), 48dBm (24dBi directional)
  5.150-5.350GHz (indoor use): 200mW (23dBm)
  5.470-5.725GHz: 1W (30dBm)
    US: 5.25-5.35: 30dBm, 5.725-5.825: 36dBm, higher for p2p

## Slide 41: Channel capacity
Transmission rate or Capacity
  In bits per second
  Rate at which data can be communicated
Bandwidth
  In cycles per second or Hertz (Hz)
  Constrained by transmitter and medium
Baud: symbols/second
  Baud  Bits per second!

## Slide 42: Nyquist Bandwidth
Noise-free channel
Limiting factor on transmission is channel bandwidth, and intersymbol interference
If bandwidth is B, highest signal rate is 2B
M different symbols encoded in log2M bits
Multi-level signaling:
  C is the data rate
  B is the bandwidth
  M is the number of levels

## Slide 43: Shannon’s Theorem
Noise creates errors
Each transmission channel corresponds to some maximum capacity C
Rate R<C can be transmitted with arbitrarily small bit error probability
  B is channel bandwidth in Hz
  S/N is signal to noise ratio at receiver

## Slide 44: Shannon’s Theorem (cont.)
Gives theoretical maximum that can be achieved
Does not indicate how it can be achieved

## Slide 45: Thermal noise
Thermal noise due to agitation of electrons
Present in all electronic devices and transmission media
Cannot be eliminated
Function of temperature

## Slide 46: Thermal noise (cont.)
Amount of thermal noise found in a bandwidth of 1Hz in any device is:
    N0 = noise power density in watts per 1 Hz of bandwidth
    k = Boltzmann's constant = 1.3803 x 10-23 J/K
    T = temperature, in kelvins (absolute temperature)
Noise is assumed to be independent of frequency
Thermal noise in bandwidth B Hertz

## Slide 47: Eb/N0 and BER
Ratio of signal energy per bit to noise power density per Hertz
Bit Error Rate (BER) for digital data is a function of Eb/N0
  Given a value for Eb/N0 to achieve a desired error rate, parameters of this formula can be selected
  As bit rate Rb increases, transmitted signal power S must increase to maintain required Eb/N0

## Slide 48: Eb/N0 and BER (cont.)
BER as function of Eb/N0 depends on modulation scheme

## Slide 49: Receiver sensitivity
Receiver sensitivity (Prx): minimum signal strength to achieve given BER
Prx=ReceiverNoiseFloor+SNR

## Slide 50: Link budget calculation
Link budget equation:
  PT: power at transmitter in dBm
  CLT: cable and connector losses at transmitter in dB
  GT: transmitter antenna gain in dBi
  PL: propagation loss in dB
  CLR: cable and connector losses at receiver in dB
  GR: receiver antenna gain in dBi
  Prx: receiver sensitivity in dBm
To achieve communication, Link Margin>Min Margin (=10-20 dB in practice)

## Slide 51: Τέλος Ενότητας # 3
Μάθημα: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 3: Ασύρματο Κανάλι και Διάδοση Σημάτων
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής