## Slide 1: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 7: Σύστημα Κινητής Τηλεφωνίας GSM και GPRS
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: GSM frequency bands (common)
GSM: Global System for Mobile Communications
GSM-900 and GSM-1800
  Europe, Middle East, Africa, most of Asia
GSM-850 and GSM-1900
  USA, Canada, other countries in America
GSM-400 and GSM-450 rarer

## Slide 3: Network architecture

## Slide 4: Network elements
Mobile Station
  Mobile Equipment
    Identified by the International Mobile Equipment Identity (IMEI)
  Subscriber Identity Module (SIM)
    Contains a unique identification number called IMSI
    It is removable, thus irrespective of a specific terminal

## Slide 5: Base Station Subsystens
Base Station Subsystem (BSS)
  Base Transceiver Station (BTS)
    A BTS is comprised of radio transceivers, antennas, the interface to the PCM facility
    BTS is the entity that connects the mobiles to a cellular network
  Base Station Controller (BSC)
    Its primary function is call maintenance, by deciding when to initiate a handover, changing the BTS transmitter power, etc.
    A BSC is connected to a group of BTSs and manages the radio resources for them

## Slide 6: Network Subsystem
Network Subsystem
  Mobile Switching Center (MSC)
    MSC provides functions such as registration, authentication, location updating, handovers and call routing to a roaming subscriber
  Home Location Register (HLR)
    The HLR contains all the administrative information and current location of each subscriber registered in the corresponding GSM network
  Visitor Location Register (VLR)
    Contains subscription information needed for call control, for all mobiles in the area of the associated MSC
  Equipment Identity Register (EIR)
    EIR is a database that contains a list of all valid mobile equipment on the network
  Authentication Center (AUC)
    Stores the secret key held in each user’s SIM card

## Slide 7: Application Service Centers
Application Service Centers are responsible for GSM network add-on services
  Operation and Maintenance Center (OMC)
    Monitoring and control the network
    Usually connect with MSC, BSC, HLR, and other service centers
  Short Message Service Center (SMSC)
    provide short message services
    usually connect to MSC
  Unstructured Supplementary Service Data Center (USSDC)
    provide USSD service in the form of *ID*ID*info#
    usually connect to HLR

## Slide 8: Protocol stack

## Slide 9: GSM FDMA/TDMA

## Slide 10: GSM channels
Physical channel: specific time slot and channel/carrier frequency
Logical channels
  run over physical channels (not necessarily in all time slots)
  two types: traffic and control
  managed: setup, maintenance, tear-down
Control channels interspersed with traffic channels in well-defined ways

## Slide 11: GSM logical channels
TCH: traffic
  full-rate
  half-rate
BCH: εκπομπής προς όλους
CCCH: ελέγχου, κοινό
DCCH: ελέγχου, ιδιαίτερο
ACCH: ελέγχου, σχετιζόμενο

## Slide 12: GSM logical channels (cont.)

## Slide 13: Traffic channels
Full rate: 22.8 kbps
  speech data: 13 kbps voice data + FEC
  packet data: 12,6,3.6 kbps + FEC
Half rate: 11.4 kbps
To achieve higher rates multiple logical channels have to be allocated (GPRS does this)

## Slide 14: Control channels
Help MS locate control channels
Provide information about
  voice and control channel repetition cycle.
  parameters in the cell
  surrounding cells
  paging
Allow random access attempts by the MS

## Slide 15: Broadcast Control Channels
FCCH (Frequency Correction Channel)
  carrier synchronization
  base station “beacon” signal
SCH (Synchronization Channel)
  frame synchronization
BCCH (Broadcast Control Channel)
  cell ID, available services, etc

## Slide 16: Common Control Channels
PCH (Paging Channel) - downlink
  page a mobile
AGCH (Access Grant Channel) - downlink
  reply to a random access request, assign dedicated control channel
RACH (Random Access Channel) – uplink
  used by mobile to request dedicated control channel
  messages from several mobiles can collide
  Slotted Aloha used for contention resolution

## Slide 17: Dedicated and Control Channels
SACCH (Slow Associated Control Channel)
  in-band signaling
  downlink: system info, power control
  uplink: measurements
FACCH (Fast Associated Control Channel)
  in-band time-critical signaling
  call establishment progress, authentication, handover signaling
SDCCH (Stand-alone Dedicated Control Channel)
  out-of-band signaling
  call setup signaling, SMS, location update

## Slide 18: Mobile initialization

## Slide 19: Location update

## Slide 20: Call origination (MS->BSS)

## Slide 21: Call termination (BSS->MS)

## Slide 22: Network elements
Mobile Station
  Mobile Equipment
    Identified by the International Mobile Equipment Identity (IMEI)
  Subscriber Identity Module (SIM)
    Contains a unique identification number called IMSI
    It is removable, thus irrespective of a specific terminal

## Slide 23: GSM identifiers
IMSI: non-dialable number
  MCC Greece: 202
  Bound to SIM
TMSI: Temporary MSI (confidentiality)
MS ISDN number (dialable)
  Different MS ISDN can be associated to same SIM

## Slide 24: Call routing
IMSI: International Mobile Subscriber Identifier
MSISDN: MS ISDN (called number)
MSRN: Mobile Station Routing Number

## Slide 25: Mobility management
Location Registration
Call delivery
Handoff Management
  Handoff is caused by:
    signal strength deterioration
    user mobility
  There are two kinds of handoff:
    soft handoff
    hard handoff
  There are three ways to handoff:
    network-controlled handoff
    mobile-assisted handoff
    mobile-controlled handoff
Rx
signal strength

## Slide 26: Three cases of handovers

## Slide 27: Power control
Operator - dependent
Mobile:
  Peak Tx power classes: GSM-900: 8,5,2,0.8 Watt (39,37,33,29 dBm), GSM-1800: 1,0.25,4 Watt (30,24,36 dBm)
  minimum Tx power: GSM-900: 19mW, GSM-1800: 15mW
  step: 2dBm
Base station:
  8 classes: 320-2.5 Watt (55-34dBm)
Base station decides power control changes for both
  Mobile measures signal strength, quality (BER) and reports to Base station
  Goal: operate at lowest power level while maintaining acceptable signal quality

## Slide 28: GPRS (General Packet Radio Service)
The major GSM Phase 2+ enhancement and an important step to 3G
  considered 2.5G
Aims at providing data services to mobile users with high bandwidth efficiency and “always on” connectivity
Address shortcomings of GSM
  Low data rates (up to 9.6 kbps)
  Long connection setup
  Expensive
  Circuit-switched

## Slide 29: GPRS (General Packet Radio Service)
The major GSM Phase 2+ enhancement and an important step to 3G
  considered 2.5G
Aims at providing data services to mobile users with high bandwidth efficiency and “always on” connectivity
Address shortcomings of GSM
  Low data rates (up to 9.6 kbps)
  Long connection setup
  Expensive
  Circuit-switched

## Slide 30: GPRS features
Data rates up to 172 kbps
Fast call setup times
“Always on” connectivity
Integrates IP infrastructure into the GSM network
Uses packet-switched mechanisms
  more efficient for bursty traffic
  allow volume-based charging

## Slide 31: Protocol architecture

## Slide 32: Channel coding & transmission rate
Coding used in every digital communication system to
  increase channel capacity
  protect against errors
GPRS uses 4 different coding schemes, depending on channel conditions
Up to 8 slots can be
combined
physical layer

## Slide 33: QoS
GPRS Release 99 specified 4 traffic classes

## Slide 34: High-level view

## Slide 35: GPRS architecture
2 new nodes .
  Serving GPRS Support Node (SGSN)
  Gateway GPRS Support Node (GGSN)

## Slide 36: Serving GPRS Support Node (SGSN)
Serving GPRS Support Node (SGSN) is responsible for:
  Admission control
  Routing, mobility management, location management, authentication, charging
  Receiving and delivering data packets
  Address translation and mapping
  Encapsulation

## Slide 37: Gateway GPRS Support Node (GGSN)
Gateway GPRS Support Node (GGSN)
  acts as interface between GPRS backbone and external Packet Data Networks (PDN) or other Public Mobile Land Networks
  converts GPRS packets coming from SGSN into the appropriate packet data protocol (PDP) format (e.g. IP)
  converts the PDP addresses of incoming data packets to the GSM address of the destination user, and sends the readdressed packet sto the responsible SGSN

## Slide 38: Additional enhancements
Base Station System (BSS): enhanced to recognize and send user data to the SGSN that is serving the area
Home Location Register (HLR): enhanced to register GPRS user profiles and respond to queries originating from SGSNs

## Slide 39: Routing Scenarios
Scenario 1: A GPRS mobile station located in PLMN 1 sends packets to a host connected to the IP network
The SGSN that the MS is registered with encapsulates the IP packets, examines the PDP context, and routes them through the intra-PLMN GPRS backbone to the appropriate GGSN
The GGSN decapsulates the packets and sends them out on the IP network
IP routing mechanisms are used to transfer the packets to the access router of the destination network. The latter delivers the IP packets to the host
Scenario 2: Assume the home-PLMN of the MS is PLMN2. The host is now sending IP packets to the MS, which are sent out onto the IP network and are routed to the GGSN of PLMN2
The GGSN of PLMN2 queries the HLR and obtains the current location of the MS (PLMN1). It encapsulates the incoming IP packets and tunnels them to the appropriate SGSN in PLMN1
The SGSN decapsulates the packets and delivers them to the MS

## Slide 40: GPRS processes
Attach process
Authentication process
PDP activation process
Detach process

## Slide 41: Enhanced Data for GSM Evolution (EDGE)
Higher data rates using 8PSK modulation
  user rate 384 kbps (GPRS: 115 kbps)
Software-only update (Release 99)
EGPRS: EDGE enhancements to GPRS

## Slide 42: EDGE higher rates
RLC data rate

## Slide 43: Τέλος Ενότητας # 7
Μάθημα: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 7: Σύστημα Κινητής Τηλεφωνίας GSM και GPRS
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής