## Slide 1: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 8: 3G UMTS, HSPA, LTE/4G, 5G Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: 1G to 5G

## Slide 3: From 2G to 3G

## Slide 4: Standardization
3rd Generation Partnership Project (3GPP)
  collaboration between telecommunication associations: ETSI, ARIB/TTC (Japan), CCSA (China), ATIS (North America), TTA (South Korea)
  develop 3G mobile system specification within scope of IMT-2000 (ITU)
  focus on radio, core network, service architecture
    GSM, UMTS 3G, HSDPA/HSUPA/HSPA,3G LTE
Different from 3GPP2
  focus on IS-95 (CDMA2000)

## Slide 5: UMTS bands

## Slide 6: UMTS architecture

## Slide 7: UMTS architecture
UTRAN is composed of several Radio Network Subsystems (RNSs) connected to the Core Network through the lu interface.
Every Radio Network Subsystem is composed of a
  Radio Network Controller (RNC).
    RNSs can be directly interconnected through the lur interface (interconnection of the RNCs).
    RNC is responsible for the local handover process and the combining/multicasting functions related to macro-diversity between different Node-Bs.
    RNC also handles radio resource management (RRM) operations.
  one or more “Node Bs”.
    A Node-B may contain a single BTS or more than one (typically 3) controlled by a site controller.
Above entities are responsible for the radio resource control of the assigned cells

## Slide 8: UTRAN: Node B
Node B (commonly called Base Station)
  comparable to Base Transceiver Station in GSM
  responsible for air interface layer
Key Node B functions
  modulation and spreading
  RF processing
  inner loop power control
  macro diversity

## Slide 9: UTRAN: RNC
RNC (Radio Network Controller) controls multiple base stations
  comparable to Base Station Controller in GSM
  layer 2 processing
  Radio Resource Management
Key functions
  outer-loop power control
  handover
  admission control
  code allocation
  packet scheduling
  macro diversity across base stations

## Slide 10: Core network
SGSN (Serving GPRS Support Node)
  The SGSN is mainly responsible for Mobility Management related issues like Routing Area update, location registration, packet paging and controlling and security mechanisms related to the packet communication
GGSN
  The GGSN node maintains the connections towards other packet switch networks such as the internet. The Session Management responsibility is also located on the GGSN.

## Slide 11: Radio Resource Management (RRM)
Handles QoS provisioning over the wireless interface
Controls cell capacity and interference in order to provide an optimal utilization of the wireless interface resources.
Includes Algorithms for Power Control, Handover, Packet Scheduling, Call Admission Control and Load Control

## Slide 12: RRM (cont)
Power Control
  Ensures that transmission powers are kept at a minimum level and that there is adequate signal quality and level at the receiving end
Packet Scheduling
  Controls the UMTS packet access
Call Admission Control
  Decides whether or not a call is allowed to generate traffic in the network
Load Control
  Ensures system stability and that the network does not enter an overload state
Handover
  guarantees user mobility in a mobile communications network

## Slide 13: Multi-Access Radio Techniques
Courtesy of Petri Possi, UMTS World

## Slide 14: Wideband CDMA
Bandwidth >= 5MHz
Multirate: variable spreading and multicode
Power control:
  open power control
  fast closed-loop power control
Frame length: 10ms/20ms (optional)

## Slide 15: WCDMA and rate
Signals from different mobiles separated based on unique codes
Transmission rate can change between frames
time
10 msec
rate can be different in different frames
received
power
frequency
5 MHz
different codes

## Slide 16: Power control in WCDMA
Fast closed-loop power control: between MS and BS
  Adjusts transmission power to achieve target signal quality (Signal-to-Interference Ratio, SIR)
  Both uplink & downlink, frequency: 1500 Hz
Uplink outer-loop power control: between BS and RNC
  Adjusts target SIR to achieve given frame error rate (data: 10-20%, voice: 1%), frequency < 100 Hz
Increase power when interference increases
Diverge when signal qualities are infeasible
fast closed-loop power control
BS
RNC
outer-loop power control (uplink)

## Slide 17: Power and rate control
WCDMA: rates fixed within single frame (10ms)
Fast closed-loop power control (Mobile-BS) operates at 1500 Hz (0.67ms)
Outer loop power control (BS-RNC) adjusts target Eb/N0 to achieve specific frame or block error rate
time
rate
power

## Slide 18: Quality of Service
Traffic Class | Conversational Class | Streaming Class | Interactive Class | Background Class
Fundamental Characteristics | Preserve time relation of (variation) between information entities of the stream Conversational pattern (stringent and low delay) | Preserve time relation of (variation) between information entities of the stream | Request response pattern Preserve payload content | Destination is not expecting the data within a certain time Preserve payload content
Example of application | voice | streaming video | web browsing | background download of emails

## Slide 19: UMTS architecture (rel99)

## Slide 20: UMTS architecture (3GPP Rel.5)

## Slide 21: UMTS all-IP

## Slide 22: 3GPP releases
Rel-99 (3/2000)
  first deployable version of UMTS
  GSM/GPRS/EDGE/WCDMA radio access
Rel.4 (3/2001)
  multimedia messaging
  efficient IP-based interconnection of core network
Rel.5 (3/2002)
  HSDPA (up to 14.4 Mbps, 1.8,3.6,7.2Mbps avail. up to 2008)
  first phase IMS
  IP UTRAN
Rel.6 (3/2005)
  HSUPA (up to 5.76 Mbps)
  enhanced MBMS
  second phase IMS
Rel. 7
  HDPA+
  flat radio access network

## Slide 23: Evolution of cellular technologies

## Slide 24: Evolution of cellular technologies
Source: 4G Americas

## Slide 25: HSDPA
High speed shared channels (15@5MHz)
  sharing in both code and time domains
Fast scheduling and user diversity
  shorter TTI (Transmission Time Interval): 2ms
Adaptive Modulation and Coding (AMC)
  Higher order modulation: QPSK and 16-QAM
  Fast link adaptation: different FEC (channel coding)
Fast hybrid ARQ
  fast combined with scheduling/link adaptation
  hybrid: combine repeated data transmissions with prior transmissions to improve successful decoding

## Slide 26: Fast scheduling and user diversity

## Slide 27: User diversity

## Slide 28: HSDPA vs. WCDMA
WCDMA
HSDPA

## Slide 29: HSUPA
Enhanced dedicated physical channel
Fast scheduling with short TTI (2ms)
Fast hybrid ARQ

## Slide 30: HSPA and HSPA+
HSPA (Rel. 6)
  DL: 14.4 Mbps, UL: 5.76 Mbps
HSPA+ goals
  exploit full potential of CDMA before moving to OFDMA (3G LTE)
  operation of packet-only mode for voice and data
HSPA+: many versions
  Rel.7 HSPA+ (DL 64 QAM, UL 16 QAM): DL: 21Mbps, UL: 11.5Mbps
  Rel.7 HSPA+ (2X2 MIMO, DL 16 QAM, UL 16 QAM): DL: 28Mbps, UL: 11.5Mbps
  Rel. 8 HSPA+ (2X2 MIMO, DL 64 QAM, UL 16 QAM): DL: 42.2Mbps, UL: 11.5Mbps

## Slide 31: Towards a simpler architecture

## Slide 32: UMTS evolution towards LTE
3G LTE: next step in evolution of 3GPP radio interfaces to deliver Global Mobile Broadband
Not 4G, but beyond 3G: 3.9G

## Slide 33: LTE targets
Increased data rates
  Peak data rate: above 100 Mbps (downlink) and 50 Mbps (uplink)
  Increase “cell edge bitrate” whilst maintaining same site locations as deployed today
Improved spectrum efficiency
  2-4X Rel 6 HSPA
Reduced latencies:
  network latency < 10 ms
  inactive-to-active latency < 100 ms
Designed for IP traffic
  Efficient support packet services (e.g. Voice over IP, Presence)
Enhanced IMS and core network
Enhanced MBMS (broadcasting)

## Slide 34: LTE targets (cont)
Spectrum and deployment flexibility
  Scaleable bandwidth: 1.25,2.5,5,10,15,20 MHz
  Both TDD and FDD modes
High mobility
  optimized for speeds 0-15 Km/h
  support high performance for 15-120 Km/h
  support mobility for 120-350 Km/h
Cost effective introduction
  Cost effective migration from Rel-6 UTRAN
  inter-working with existing 3G and non-3GPP systems (WiMAX, WLAN)
  simplified Radio Access Network (RAN)

## Slide 35: LTE features
Downlink based on OFDMA
Uplink based on SC-FDMA
only packet switched
  no circuit switched connectivity
MIMO: use more than one TX/RX antennas

## Slide 36: Evolution > 2012

## Slide 37: LTE Advanced (Rel. 12)
Source: 4G Americas, 2015

## Slide 38: Air interface technologies

## Slide 39: MIMO and carrier bandwidth

## Slide 40: Latency comparison

## Slide 41: LTE Radio Access Network
UMTS:
LTE:
Evolved-UTRAN

## Slide 42: 3G LTE Evolved-UTRAN

## Slide 43: LTE simplified architecture
Evolved UTRAN (EUTRAN):
Most RNC functionalities moved to eNodeB
RNC removed
eNodeB connects to evolved packet core

## Slide 44: Spectral efficiency
Source: 4G Americas, 2015

## Slide 45: Proximity Services (LTE Rel. 12)
Direct discovery: identifies UE that are in direct proximity of each other
Direct communication: device-to-device communication between UEs
  both in presence and in absence of LTE network

## Slide 46: Direct Discovery
Type 1: UE selects resource from resource pool
Type 2B: LTE network allocates resources

## Slide 47: Direct Communication
Mode 1: LTE network explicitly assigns resources
Mode 2: UEs select resources for control & data from resource pool

## Slide 48: Small cells

## Slide 49: Small cell challenges

## Slide 50: Small cell approaches

## Slide 51: Types of cells

## Slide 52: Partnerships and Forums
ITU IMT-2000 http://www.itu.int/imt2000
Mobile Partnership Projects
  3GPP: http://www.3gpp.org
  3GPP2: http://www.3gpp2.org
Mobile Technical Forums
  3G All IP Forum: http://www.3gip.org
  IPv6 Forum: http://www.ipv6forum.com
Mobile Marketing Forums
  Mobile Wireless Internet Forum: http://www.mwif.org
  UMTS Forum: http://www.umts-forum.org
  GSM Forum: http://www.gsmworld.org
  Universal Wireless Communication: http://www.uwcc.org
  3G Americas: http://www.3gamericas.org
  Global Mobile Supplier: http://www.gsacom.com

## Slide 53: Τέλος Ενότητας # 8
Μάθημα: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 8: 3G UMTS, HSPA, LTE/4G, 5G
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής