## Slide 1: Ασύρματα Δίκτυα και Κινητές Επικοινωνίες
Ενότητα # 2: Επισκόπηση και Τάσεις
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Fixed versus mobile broadband

## Slide 3: Mobile traffic volume

## Slide 4: Traffic volume and devices

## Slide 5: Number of devices

## Slide 6: Traffic type

## Slide 7: Cellular technologies

## Slide 8: Evolution

## Slide 9: Wired versus wireless
source: Huawei

## Slide 10: Uplink versus downlink

## Slide 11: Mobile network evolution
1st Generation
  Analogue mobile phone (e.g., AMPS, NMT)
  Low quality speech, low speed data 2.4 kbps
2nd Generation
  Digital mobile (e.g., GSM)
  Digital voice, low speed data (9.6 kbps)
Generation 2.5 [2.5G]
  Packet switching data, Internet access
    e.g., GPRS
  higher data-rates
    10…171.2 kbps, in theory, ~40 kbps in practice

## Slide 12: Mobile network evolution (cont)
3rd Generation [3G]
    (digital) multimedia (e.g., UMTS)
    Higher data-rate (144 kb/s … 2 Mb/s, in theory)
    HSDPA, HSUPA, HSPA
    Interoperation with 2G and national roaming
4th Generation [4G]
    Seamless High-speed wireless Internet access (e.g., LTE-Advanced, IEEE 802.11n, mobile WiMAX, 802.16e)
      IP based communication (11 … 54 Mb/s)
    Short range, high capacity Wireless Internet Access (1 Gb/s)
    “virtual reality” connection to the Internet

## Slide 13: Wireless Evolution
Unlicensed spectrum
WLANs 802.11: 802.11b, 802.11g/a, 802.11n (~150-300Mbps), 802.11ac (~300-900Mbps)
Metropolitan/community wireless networks, opportunistic device-to-device communication

## Slide 14: Wired vs. wireless
wired: very low attenuation, no interference, low bit error probability, high deployment cost (digging)
wireless: high attenuation, interference, high bit error probability, low deployment cost

## Slide 15: Packet-based future

## Slide 16: Service provision model trends
2G
3G
4G
Service provider
Transport provider
Subscriber
Access provider
GSM Operator
Content provider
Content Aggregator
Service provider
Transport provider
Subscriber
Access provider
UMTS Operator
Content provider
Content Aggregator
Service provider
Transport provider
Access provider
Subscriber
Application provider
Access provider
Mediator
User
User
User
Στατική σύνδεση πρόσβασης και υπηρεσίας
Νέος ρόλος για χρηστο-κεντρική παροχή πρόσβασης και υπηρεσιών

## Slide 17: Εξέλιξη τερματικών και ασύρματων τεχνολογιών διεπαφής
Διαφοροποίηση
2G
3G
4G
«Κάθετες» υπηρεσίες
  Τηλεφωνία
  Συμπληρωματικές υπηρεσίες
  Φαξ
Direct Sequence
Frequency Hopping
WCDMA
TD-CDMA
TDMA
FDD
OFDM
TDD
OFDM
Java Standard Edition
Personal Java
Java Micro Edition
WAP
«Οριζόντιες» υπηρεσίες
  Βασισμένες στο IP
  Προστιθέμενη Αξία
«Κλειστή» παροχή υπηρεσίας
«Ανοικτή» παροχή υπηρεσίας

## Slide 18: NetworkS of the future
Satellite
Micro-Cell
Urban
In-Building
Pico-Cell
Global
Suburban
Home-Cell
Macro-Cell
dik

## Slide 19: Interconnection at multiple layers

## Slide 21: Mobile traffic offloading

## Slide 22: Mobile communications and the Internet
Internet targets
Will be available everywhere
Will be available all the time
Will be open
Will be possible to access it from any device

## Slide 23: Mobile communications and the Internet
Key assumption that Internet got wrong:
The end-user, his access terminal, and his network address
  are all bound
  and remain in the same position

## Slide 24: Key high-level trend
Mobile telephony
Mobile Internet access
Seamless information access

## Slide 25: Mobile networking applications
Music/video streaming
Social networks
Content downloading
Web browsing
Cloud services
  Synchronization and backup
  Cloud-hosted apps
  Music/video streaming
  Machine-to-machine
  Mobile commerce

## Slide 26: Trends
Ubiquitous wireless access
  access in different areas
  wireless embedded in devices/sensors
  heterogeneous air interfaces
  unlicensed spectrum
Fixed-Mobile convergence
  4-play and n-play bundles
Wireless technologies
  MIMO
  OFDMA
Wireless Architectures
  cross-layer network stack
  All-IP
  pico cells
  Mesh/Ad Hoc

## Slide 27: Trends (cont)
Open-everything
  Open-access
  Open-spectrum
  Open mobile phone OS (e.g. Android)
  Open network device OS (e.g. Openflow)
Web-Cloud services
  thing clients
  mobile-web convergence
Mobile social networks
Location/presence-based services
  searching

## Slide 28: Challenges
Wireless
  limited bandwidth
  variable and asymmetric link quality
  easier to snoop and malicious attacks
  heterogeneous air interfaces
Mobility
  varying location
  varying connectivity
  varying speed
  easier to spoof
  limited resources (battery, processing, storage)

## Slide 29: Challenges: technical
open/dynamic spectrum
adaptability
  to connectivity, location, spectrum availability, etc
  of both network and end-user devices
  software defined radio (SDR)
cross-layer and cross-mechanism optimization
opportunistic forwarding/routing
multipath and network coding

## Slide 30: Wireless architectures
Cellular
  hierarchical RAN (Radio Access Network)
  moving towards flat, peer-to-peer, mesh
WLAN
  local connectivity (until now)
  dense deployments
Wireless multihop
  Ad Hoc: infrastructure-less
  Wireless Mesh Networks: GateWays connecting to fixed network
Sensor networks

## Slide 31: 3G/UMTS Hierarchical Radio Access Network (RAN)

## Slide 32: WiMAX (IEEE 802.16) RAN with relaying

## Slide 33: 3G Long Term Evolution (LTE) RAN

## Slide 34: Wireless Mesh Network

## Slide 35: Infrastructure vs. infrastructure-less networks
Cellular, WLANs
  rely on infrastructure (=planning)
Ad hoc networks
  no infrastructure
  no connection to fixed network
Wireless mesh networks
  wireless multi-hop
  have connection to fixed network

## Slide 36: MANET

## Slide 37: MANETs vs. WMNs
Mobile Ad Hoc Networks (MANETs)
user devices are also intermediate nodes (perform forwarding)
both end and intermediate nodes are mobile
no connection to fixed network
connectivity primary issue
devices have single wireless interface
Wireless Mesh Networks (WMNs)
only intermediate mesh nodes only perform forwarding
only end-user devices are mobile; mesh nodes are fixed
one or more connections to fixed network
reliability, throughput, and delay important
devices can have multiple wireless interfaces

## Slide 38: Wireless Embedded and Sensor Networks
embedded device: a device with a computer, which are not a computer themselves
embedded wireless device: a device with a wireless interface built in
Features
  both sensing and actuation
  interact with environment and people
  constrained resources (processing, power, storage)
WSNs: isolated
WENs: connected to Internet
  renewed interest in IPv6-based

## Slide 39: Τέλος Ενότητας # 2
Μάθημα: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 2: Επισκόπηση και Τάσεις
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής