## Slide 1: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 9: Σύγκλιση Σταθερών και Κινητών Επικοινωνιών (Fixed-Mobile Convergence)
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Convergence drivers

## Slide 3: Fixed-Mobile Convergence drivers
Ubiquitous, personalized services across multiple domains
Reduction of operation costs through all-IP infrastructure
  bandwidth has become a commodity
Unified network allows optimization for
  efficient service delivery to users
  ease of internetworking with partners and other networks
  efficient and reduced OPEX
Revenue increasingly driven by services and content, rather than network type

## Slide 4: End-user drivers
Customization and personalization
  single device supports multiple user profiles
  personalization of single service: one-size does not fit all
Blending
  interworking of different services
User awareness
  presence information: availability, location
  adapt to device and network capabilities
Flexibility
  in terms of device
  in communicating most convenient way and time
  in terms of price
Simplicity
  single address/number
  consistent user interface
  consolidated service administration

## Slide 5: Telecommunications market growth
(Year -end)
Fixed Broadband
(Cable, xDSL,Ethernet)
Fixed
(POTS/ISDN)
Mobile
Source: Internal Ericsson
slower rate of increase

## Slide 6: Mobile operators
Significant growth
Saturation of voice-centric revenue
  price competition
  lower average revenue per subscriber
Need new ways to generate revenue and maintain customer base
  high speed data services
  other services e.g. bundles (with fixed), video, gaming
Huge demand for data transfer (Internet)

## Slide 7: Wireline operators
Traditional subscriber base eroded
  VoIP
  lowering prices for mobile telephony
Fixed services typically regulated
  wireline operators less adaptable
New services
  triple/quad-play (quad: data,voice,video/TV,wireless)
  hotspot (WiFi) services

## Slide 8: Other types of operators
Virtual Network Operators (VNOs)
Content providers
Increased opportunities

## Slide 9: FMC goal
Operator: migrate today’s separate circuit and packet switch core networks to a unified core network that supports existing access technologies in both the fixed and mobile domains
use of common components and service specific extensions that reduce the cost of service development and implementation

## Slide 10: Convergence at multiple layers

## Slide 11: User services
Consolidation: All multimedia services become available via a single subscription — device and client. End-user experiences reduced complexity when managing communications
Simplification: Overall service is simplified with a consistent look and feel, single address book and web-based provisioning. End-user finds the overall service more usable
Enrichment: Service set can be enriched with presence, personalization and network-based content

## Slide 12: FMC key technologies
VoIP
SIP
IP Multimedia Subsystem (IMS)
Unlicensed Mobile Access (UMA)
Fixed and Wireless Broadband Access

## Slide 13: Session Initiation Protocol (SIP)
Common IP-based network framework
Originally defined by IETF, then adopted by 3GPP
Basic features
  peer-to-peer signaling protocol
  initiates, terminates, modifies sessions
  session: two-way voice communication, multimedia conference, instant messaging, application sharing
  not a vertical solution: utilizes other protocols for transport, QoS, accounting, etc

## Slide 14: IMS
Supports multimedia services over multiple access technologies UMTS,GSM,fixed broadband, WLAN

## Slide 15: IMS architecture

## Slide 16: IMS components

## Slide 17: IMS standard interfaces

## Slide 18: Unlicensed Mobile Access (UMA)
Goal to leverage unlicensed wireless and wired access
Tunnel GSM voice over WLAN/Bluetooth and IP network
  authentication handled by mobile network
  Standardized by 3GPP as Generic Access Network (GAN)

## Slide 19: Femtocells
Femtocell: 3G access point
Reduce distance => reduce power, improve coverage
Does not require dual-mode handsets (unlike UMA)
Three alternatives core network connection
  RNC connection (lu-b) over IP
  UMA-based
  IMS-based

## Slide 20: RNC connection (lu-b) over IP

## Slide 21: UMA-based

## Slide 22: IMS-based

## Slide 23: Challenges
Business relationships
  changing landscape and need for new business models
Quality of Service
  heterogeneous networks with different resource availability
Regulatory issues
  changing regulatory environment and lack of regulatory framework e.g. for VoIP and service bundling
Device availability
  non-standard services do not help economies of scale
  standardization proceeds slowly

## Slide 24: Operator evolutionary strategies
Service bundling
  increases customer loyality
IP network convergence
  IP-based service platforms
  increase service deployment efficiency
Service convergence
  full service convergence improves user experience and ease of use
Operator and organizational convergence
  leverage assets in different domains

## Slide 25: Τέλος Ενότητας # 9
Μάθημα: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 9: Σύγκλιση Σταθερών και Κινητών Επικοινωνιών
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής