## Slide 1: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 10: Mobile Network Layer: Mobile IP
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Motivation for Mobile IP
Internet started at a time when mobile computers did not exist
  Internet today lacks mechanisms for supporting mobile users
  IP is common base for many applications running over different networks
Mobile IP adds mobility support to IP
Key issue: Routing
  Destination network prefix determines physical subnet
  Change of physical subnet requires change of IP address

## Slide 3: Supporting mobile nodes
Create routes to mobile nodes?
  Change all routing table entries to forward packets to destination mobile node
  Scalability issues due to number of mobile nodes and frequent location changes
Change IP address when mobile moves?
  Need to modify IP address depending on location
  Impossible to find mobile host; DNS not built for frequent updates
  TCP connection breaks

## Slide 4: Mobile IP requirements
Transparency
  Mobile nodes keep IP addresses
  Point of connection to fixed network can change
  Communication continues after link interruption
Compatibility
  Support same layer 2 protocols as IP
  No changes to end systems and routers
  Mobile nodes can communicate with fixed nodes

## Slide 5: Mobile IP requirements (cont.)
Security
  Authentication of registration messages
Efficiency
  Few additional messages
Scalability
  Global support for large number of mobile nodes

## Slide 6: Real life analogy
What happens when you move to a new house?
  Leave forwarding address to your old post office
  Old post office forwards your mail to new post office
  New post office delivers it to you
Mobile IP implements above procedure!

## Slide 7: Mobile IP actors
Mobile Node (MN)
  Can change point of attachment to fixed network without changing IP address (Home address is static)
  New Care-of Address (CoA) associated with new network attachment point
Correspondent Node (CN)
  Node wishing to communicate with mobile node

## Slide 8: Mobile IP actors (cont.)
Home Agent (HA)
  System in home network of MN, usually router
  Maintains current location of MN (CoA)
  Tunnels IP packets to MN’s CoA
Foreign Agent (FA)
  System in foreign network, usually router
  Receives IP packets from HA
  Forwards IP packets to MN

## Slide 9: Mobile IP mechanisms
Discovering the care-of address
Registering the care-of address
Tunneling packets to the care-of address

## Slide 10: Discovering Care-of Address
Built on top of existing ICMP router advertisements
Router advertisements extended to carry available CoAs: agent advertisements
Foreign (& home) agents periodically broadcast agent advertisements
Mobile host can choose not to wait for advertisement and send solicitation message
  If MH doesn’t hear its current CoA from foreign agent, it seeks another CoA

## Slide 11: Agent advertisements
Allows detection of mobility agents
Lists one or more available care-of addresses
Informs mobiles about special features
Mobile node checks whether agent is home agent or foreign agent

## Slide 12: Agent advertisement message

## Slide 13: Registering Care-of Address
Once mobile host receives CoA it registers it with its home agent
  Registration request goes through foreign agent
Home agent approves request and responds with a registration confirmation
  Security is important
Registration has limited lifetime

## Slide 14: Registering Care-of Address (cont.)

## Slide 15: Securing the registration procedure
Home agent must be certain registration was originated by mobile node
Security association based on Message Digest 5 (MD5)
Use of timestamps or random numbers to avoid replay attacks

## Slide 16: Home agent discovery
Agents operate both as home and as foreign agents
Home agents periodically send agent advertisements
Mobile listens to agent advertisements to determine if it is in its home network or a foreign network
If mobile is unable to communicate with home agent it broadcasts a home agent discovery message

## Slide 17: Tunneling to the care-of-address

## Slide 18: Mobile IP tunneling and response from mobile node

## Slide 19: Problems with Mobile IP
Routing inefficiencies
  Asymmetric routing (triangular routing)
  Reverse tunneling
    Solves issue with topologically correct sender addresses
    Still inefficient since all packets (forward and reverse) go through home agent
  Deliver care-of-address to correspondent node
    Requires changes to end nodes that are not mobile
Security
  Authentication of foreign agent
Packets can be lost when mobile changes network attachment point (handoff)

## Slide 20: Mobile IP and IPv6
Mobile IP was developed for IPv4, but IPv6 simplifies things
  Security is integrated and not an add-on; IPv6 nodes implement strong authentication/encryption
  CoAs can be assigned using auto-configuration
  No need for separate foreign agents; all routers perform router advertisements, which can be used instead of agent advertisements
  A mobile node can send the CoA directly to correspondent node (route optimization)

## Slide 21: IP micro-mobility
Micro-mobility support
  Efficient local handover in foreign domain without involving home agent
  Reduces control traffic on backbone
  Needed in case of route optimization
Approaches
  Cellular IP
  HAWAII
  Hierarchical Mobile IP

## Slide 22: Cellular IP
Operation
  CIP Nodes maintain routing entries (soft state) for MNs
  Multiple entries possible
  Routing entries updated based on packets sent by MN
CIP gateway
  Mobile IP tunnel endpoint
  Initial registration processing
Security
  All CIP Nodes share network key
CIP Gateway
Internet
BS
MN1
data/control
packets
from MN 1
Mobile IP
BS
BS
MN2
packets from
MN2 to MN 1

## Slide 23: Network mobility
Mobility support for entire networks of IP devices
  E.g. trains, airplanes, cars, personal area networks
IETF NEMO (Network Mobility) extends Mobile IP
  Mobile Router (MR) takes role of mobile node in performing mobility functions
  Mobile network nodes are not aware of mobility and do not perform mobility functions
  Home agents bind entire network prefix to MR’s care-of address

## Slide 24: Bigger picture: identifiers & locators
IP addresses serve a dual role:
  Identifiers of host interfaces
  Locators for topological locations used for routing IP packets
Above duality makes some things hard
  Mobility
  Multi-homing
  Security/privacy, etc
Proposals to separate ID & locator: Locator/ID Separation Protocol (LISP), Host Identity Protocol (HIP), etc

## Slide 25: Τέλος Ενότητας # 10
Μάθημα: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 10: Mobile Network Layer: Mobile IP
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής