## Slide 1: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 13: Mobility Support in Information Centric Networking (ICN)
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής

## Slide 2: Three network generations

## Slide 3: Problems with Current Internet
End-to-end semantics is not the prevailing usage paradigm
  Information-centricity: focus on information itself not where it resides
  Overlay content delivery structures (CDNs, P2P): ignore network topology and requester/data location
  Firewalls, NATs, proxy servers
  ISPs: costly (Deep Packet Inspection-DPI) to find type of information
Mobility support not seamless
  IP addresses used both as host and location identifiers

## Slide 4: Problems with Current Internet (cont.)
Security and trust
  Sender controlled transport facilitates DoS attacks
  Focus on communication security, but information security can be more important
Run-time tussles between various players
  Imbalance of power – functions not separated when they should be (e.g. well-known port numbers and applications)
  Ossification of architecture with point solutions/patches
Congestion control
  End-to-end semantics not appropriate when links have different and variable network conditions
  flash crowds

## Slide 5: Principles of Information-Centric Networking (ICN)
Naming of content rather than hosts/interfaces
  Departs from host-to-host communication model
  Content independent of devices that store it
  Names are location independent
Receivers (subscribers) request content
  Receiver control
Sources (publishers) advertise content
  Need to match requests to advertised content
Receivers and senders
  do not have to be aware of each other, and
  are decoupled in time

## Slide 6: Basic Functions of ICN
Name resolution: Match requests to content advertisements
Routing (topology formation): Determine path from source (publisher) to receiver (subscriber)
Forwarding: Transfer content from source to receiver
Data Transfer = Routing + Forwarding
Resolution Network
Source
Receiver
Forwarding Node
Different degree of coupling between resolution & data transfer

## Slide 7: … but isn’t previous picture an IP network ?
ICN principles make the difference:
Naming of content rather than hosts/interfaces
  DNS: location-dependent names
  IP: location-dependent addresses used as both host & location identifiers
Receivers (subscribers) request content
  IP: sender has all power
Sources (publishers) advertise content and network matches requests to content advertisements
  IP: user needs to know or find out where to get content
Receivers & senders don’t have to be aware of each other
  IP: both sides of a connection know other side’s location-dependent address

## Slide 8: Key Advantages & Features of ICN
Receiver mobility support
In-network caching
Content-aware traffic management
Hop-by-hop transport & congestion control
One-to-many/any and many/any-to-one communication modes
ICN architecture proposals differ in degree of coupling between
  name resolution & data transfer
  data routing & forwarding

## Slide 9: Name Resolution and Data Transfer
Different degree of coupling between resolution & data transfer
Decoupled: different nodes perform resolution & data transfer (similar to DNS)
Coupled: nodes perform resolution and data transfer
Resolution Network
Source
Data Transfer = Routing + Forwarding
Receiver
Forwarding Node

## Slide 10: Decoupled Resolution & Data Transfer
Resolution function matches requests to sources or caches (in-network caches)
Data path independent of request (control) path
Source or Cache
Receiver
Information request
Data Transfer
Resolution Network
Forwarding Node
name
data
Examples: PSIRP/PURSUIT, NetInf/SAIL

## Slide 11: Coupled Resolution & Data Transfer
Nodes route information requests to source or cache (in-network caching)
Data path inverse of request (control) path
Data Transfer
Source or Cache
Receiver
Forwarding Node
Information Request
name
data
Examples: CCN/NDN, DONA, COMET, Convergence

## Slide 12: Tradeoffs from different coupling of Name Resolution & Data Transfer
Coupled
  Data path reverse of request (control) path
  In-network caching simpler through local mechanisms for routing requests
Decoupled
  Support for advanced policies (e.g. QoS, interconnection agreements)
    Implemented by one function without affecting the other
  Exploitation of different paths for control & data (e.g. low-delay path for control and high bandwidth path for data)
  Separation of functions addresses tussles & allows competition
  More choices for supporting source mobility

## Slide 13: Receiver mobility
Receiver mobility supported by design:
Receiver-driven content request model
No end-to-end session establishment such as TCP
Individual chunks/packets are named hence can be requested individually
Receiver
old location
Source
Receiver
new location
Information Request

## Slide 14: Receiver mobility and caching
In-network caching can assist receiver mobility
Caches along path followed by request can provide data
  Possible with naming of content chunks/packets
Further optimization: use caches proactively
Source
Receiver
new location
Receiver
old location
Data Transfer

## Slide 15: Receiver mobility & proactive caching
Transfer content requests to one-hop neighbors
  Prefetch content at neighbors when mobile disconnects
Wasted resources if we prefetch content to all neighbors
Select subset of neighbors based on transition probability  Selective Neighbor Caching (SNC)
Source
Receiver

## Slide 16: Receiver mobility & proactive caching
Transfer content requests to one-hop neighbors
  Prefetch content at neighbors when mobile disconnects
Wasted resources if we prefetch content to all neighbors
Select subset of neighbors based on transition probability  Selective Neighbor Caching (SNC)
Source
Higher prob to move to green PoA than to red
Receiver

## Slide 17: Source mobility
Not as straightforward as receiver mobility
  Receiver-driven (pull) model helps receiver mobility
  Requests need to be “matched” to sources
  Requests contain location-independent names
Two problems need to be addressed
  Find source’s new location: to forward content requests
  Achieve session continuity: reduce or avoid service disruption and data loss/delay

## Slide 18: Source mobility approaches
Routing-based approach
  Routing tables updated when source moves
  Only solution if no location-dependent addresses
Indirection approach
  Agents at home and visited network
  Need location-dependent addresses
Resolution approach
  Requires separate resolution function

## Slide 19: Source mobility: routing-based
Requests forwarded using routing tables
Routing tables populated based on content advertisements
Source mobility would trigger new content advertisements. Issues:
  Convergence time
  Routing table scalability
  Smaller problem in case of micro-mobility
Optimization: Proactive content advertisements
How data is forwarded from source to receiver depends on specific architecture
Source
old location
Source
new location
Receiver
n1
n1
n1

## Slide 20: Source mobility: indirection approach
Home agent forwards requests to new source location
  Requires location-dependent identifiers
  Similarities with Mobile IP
Agents in visited network can help transparency
  Automatically add location prefixes
Disadvantages:
  Communication goes through home agent
Source
old location
Source
new location
Receiver
Home
agent
n1
PoA
n1
n1

## Slide 21: Source mobility: indirection approach
Home agent forwards requests to new source location
  Requires location-dependent identifiers
  Similarities with Mobile IP
Agents in visited network can help transparency
  Automatically add location prefixes
Disadvantages:
  Communication goes through home agent
Source
old location
Source
new location
Receiver
Home
agent
n1
PoA/n1
PoA
n1
n1

## Slide 22: Source mobility: resolution approach
Resolution function already exists when resolution and data transfer decoupled
Resolution table updated with current location  need location-dependent ids
Separation of identity-locator not new: Host Identity Protocol (HIP), Identifier-Locator Network Protocol (ILNP)
Source
old location
Source
new location
Receiver
n1
n1
PoA
Resolution function

## Slide 23: Source mobility: resolution approach (2)
Resolution function can be provided by
  Independent resolution network
  Home agent
Issue: Resolution overhead, only for first communication
How data is forwarded from source to receiver depends on specific architecture
Source
old location
Source
new location
Receiver
n1
n1
PoA
Resolution function

## Slide 24: Source mobility: resolution approach based on home agent
Home agent: binding between name and location
  Location id: PoA prefix+name
  Updated when source moves
Request for content n1 routed to home agent
Home agent responds with PoA/n1
Receiver requests PoA/n1
Source
old location
Source
new location
Receiver
Home
agent
PoA

## Slide 25: Source mobility: resolution approach based on home agent
Home agent: binding between name and location
  Location id: PoA prefix+name
  Updated when source moves
Request for content n1 routed to home agent
Home agent responds with PoA/n1
Receiver requests PoA/n1
Source
old location
Source
new location
Receiver
n1
Home
agent
PoA

## Slide 26: Source mobility: resolution approach based on home agent
Home agent: binding between name and location
  Location id: PoA prefix+name
  Updated when source moves
Request for content n1 routed to home agent
Home agent responds with PoA/n1
Receiver requests PoA/n1
Source
old location
Source
new location
Receiver
n1
Home
agent
PoA
PoA/n1

## Slide 27: Source mobility: resolution approach based on home agent
Home agent: binding between name and location
  Location id: PoA prefix+name
  Updated when source moves
Request for content n1 routed to home agent
Home agent responds with PoA/n1
Receiver requests PoA/n1
Source
new location
Source
old location
Receiver
Home
agent
PoA
PoA/n1

## Slide 28: Source mobility: session continuity
Mechanisms at mobile nodes help
  Moving node informs other side that it will move and possibly where it will move
Home/visited agents can help achieve transparency
  Automatically add PoA prefix
  No changes to mobile nodes

## Slide 29: Conclusions
Receiver mobility supported by design in ICN
  Optimizations are possible by exploiting caches
Source mobility is more difficult in ICN
  With location-independent names only routing-based approach is possible
    Convergence time and routing table scalability issues
  Location-dependent identifiers necessary to support efficient source mobility in the general case
Both location-independent names and location-dependent addresses have a role in future networks
Flexible/dynamic mapping and usage of names and addresses to find & transfer information is key

## Slide 30: Τέλος Ενότητας # 13
Μάθημα: Ασύρματες και Κινητές Επικοινωνίες
Ενότητα # 14: Mobility Support in Information Centric Networking (ICN)
Διδάσκων: Βασίλειος Σύρης
Τμήμα: Πληροφορικής